## Slide 1: TE2003B SoC Design: Computer organisation & architecture Computer Arithmetic

## Slide 2: References
The following material has been adopted and adapted from
Patterson, D. A., Hennessy, J. L., Computer Organization and design: The hardware/software interface – ARM edition, Morgan Kaufmann, 2017.
S. L. Harris and D. M. Harris, Digital design and computer architecture - ARM edition, Morgan Kaufmann, 2016.
J. Yiu, The definitive guide to ARM Cortex-M0 and Cortex-M0+ processors, Second edition, Elsevier, 2015.

## Slide 3: Arithmetic for Computers
Operations on integers
Addition and subtraction
Multiplication and division
Dealing with overflow
Floating-point real numbers
Representation and operations

## Slide 4: Integer operations

## Slide 5: Two’s complement review
Assume two’s complement format
  Q: What’s the range (minimum and maximum values that can be represented) of an N-bit two’s complement number?
    A:
    For example, an 8-bit two’s complement number may represent values in the range
    =

## Slide 6: Overflow & underflow
Q: What is overflow?
  A: A condition when the result of a calculation exceeds the maximum value that can be represented in a numeric format.
Q: What is underflow?
  A: A condition when the result of a calculation is smaller than the minimum value that can be represented in a numeric format.
Sometimes, the term overflow is used for describing both conditions.

## Slide 7: Addition

## Slide 8: Integer addition
Example: 7 + 6
Overflow if result out of range
  Adding +ve and –ve operands, no overflow
  Adding two +ve operands
    Overflow if result sign is 1
  Adding two –ve operands
    Overflow if result sign is 0
(+7)
(+6)
(+13)

## Slide 9: Integer addition
Example: Adding two 4-bit two’s complement numbers
5 + 1
+5: 0101 +1: 0001 +6: 0110
3 + 6
+3: 0011 +6: 0110 -7: 1001
–2 + 5
-2: 1110 +5: 0101 +3: 0011
–7 +(–1)
-7: 1001 -1: 1111 -8: 1000
–3 +(–6)
-3: 1101 -6: 1010 +7: 0111
Overflow:+9 and -9
can not be represented in 4-bit
two’s complement.

## Slide 10: Subtraction

## Slide 11: Integer subtraction
Addition with negation of second operand
Example: 7 – 6 = 7 + (–6)
  +7: 0000 0000 … 0000 0111 –6: 1111 1111 … 1111 1010 +1: 0000 0000 … 0000 0001
Overflow if result out of range
  Subtracting two +ve or two –ve operands, no overflow
  Subtracting +ve from –ve operand
    Overflow if result sign is 0
  Subtracting –ve from +ve operand
    Overflow if result sign is 1

## Slide 12: Integer subtraction
Example: Subtracting two 4-bit two’s complement numbers
5 – (+1)
+5: 0101 -1: 1111 +4: 0100
–3 – (+6)
-3: 1101 -6: 1010 +7: 0111
–2 – (–5)
-2: 1110 +5: 0101 +3: 0011
7 –(–1)
+7: 0111 +1: 0001 -8: 1000
Overflow: -9 and +8 can not be represented in 4-bit two’s complement.

## Slide 13: Addition & subtraction overflow summary
Overflow conditions for additions and subtraction in two’s complement.

## Slide 14: Multiplication

## Slide 15: Multiplication
Start with long-multiplication approach
1000
× 1001
1000
0000
0000
1000
01001000
Length of product is the sum of operand lengths.
multiplicand
multiplier
product
What can be improved in this architecture?
Assume we want to multiply two 64-bit numbers

## Slide 16: Multiplication hardware
Initially 0
64th repetition?
LSB
There’s one error in the flow chart. Can you spot it?
What can be improved in this architecture?

## Slide 17: Multiplication hardware
LSB
This architecture has a major flaw.
Can you spot it?
For multiplying two N-bit number, it requires:
Two 2N-bit registers
One N-bit register
A 2N-bit ALU
This is a waste of resources!

## Slide 18: Optimised multiplier
Perform steps in parallel: add/shift
One cycle per partial-product addition
  That’s ok, if frequency of multiplications is low
For multiplying two N-bit number, it requires:
One N-bit register
One 2N-bit register
An N-bit ALU

## Slide 19: Optimised multiplier
Load lower half of Product with Multiplier
Add multiplicand to upper half of product
Shift product right
Start
End
YES
Nth repetition?
NO
YES
P[0] == 1?
NO

## Slide 20: Optimised multiplier - example
Multiplicand = : 1111
Multiplier = 1101
1111
0000 1101
STEP 0: Initialize registers
Multiplier loaded into lower half of product
4-bit ALU

## Slide 21: Optimised multiplier - example
Multiplicand = : 1111
Multiplier = 1101
1111
STEP 1:
Product LSB == 1 : Add
Right shift product
0000
0 1111
01111 1101
4-bit ALU

## Slide 22: Optimised multiplier - example
Multiplicand = : 1111
Multiplier = 1101
1111
0111 1110
STEP 1:
Product LSB == 1 : Add
Right shift product
4-bit ALU

## Slide 23: Optimised multiplier - example
Multiplicand = : 1111
Multiplier = 1101
1111
0111 1110
STEP 2:
Product LSB == 0 : No Add
Right shift product
4-bit ALU

## Slide 24: Optimised multiplier - example
Multiplicand = : 1111
Multiplier = 1101
1111
0011 1111
STEP 2:
Product LSB == 0 : No Add
Right shift product
4-bit ALU

## Slide 25: Optimised multiplier - example
Multiplicand = : 1111
Multiplier = 1101
1111
STEP 3:
Product LSB == 1 : Add
Right shift product
0011
1 0010
1 0010 1111
4-bit ALU

## Slide 26: Optimised multiplier - example
Multiplicand = : 1111
Multiplier = 1101
1111
STEP 3:
Product LSB == 1 : Add
Right shift product
1001 0111
4-bit ALU

## Slide 27: Optimised multiplier - example
Multiplicand = : 1111
Multiplier = 1101
1111
1001
1 1000
STEP 4:
Product LSB == 1 : Add
Right shift product
1 1000 0111
4-bit ALU

## Slide 28: Optimised multiplier - example
Multiplicand = : 1111
Multiplier = 1101
1111
1100 0011
STEP 4:
Product LSB == 1 : Add
Right shift product
4-bit ALU

## Slide 29: Optimised multiplier - example
Multiplicand = : 1111
Multiplier = 1101
1100 0011
After 4 steps, final result will be in Product register
1100 0011 =
4-bit ALU

## Slide 30: Signed multiplication
So far, we’ve only dealt with unsinged operands.
What happens in signed multiplication?
For adding two signed N-bit numbers:
  Convert both multiplicand and multiplier to positive numbers and keep track of their respective sign.
  Apply multiplication algorithm N-1 times.
  Negate product if signs are not the same.
Alternatively, previous algorithm works for signed numbers as long as shifts are performed using sign extension.

## Slide 31: Faster Multiplier
Uses multiple adders
  Cost/performance tradeoff
Use (N-1) N-bit adders in parallel, instead of a single N-bit adder (N-1) times.
Can be pipelined
  Several multiplication performed in parallel

## Slide 32: Division

## Slide 33: Division
Check for 0 divisor
Long division approach
  If divisor ≤ dividend bits
    1 bit in quotient, subtract
  Otherwise
    0 bit in quotient, bring down next dividend bit
Restoring division
  Do the subtract, and if remainder goes < 0, add divisor back
Signed division
  Divide using absolute values
  Adjust sign of quotient and remainder as required
1001
1000 1001010
-1000
10
101
1010
-1000
10
n-bit operands yield n-bit quotient and remainder
quotient
dividend
remainder
divisor

## Slide 34: Division hardware
Initially dividend
Initially divisor in left half

## Slide 35: Optimized divider
One cycle per partial-remainder subtraction
Looks a lot like a multiplier!
  Same hardware can be used for both

## Slide 36: Faster Division
Can’t use parallel hardware as in multiplier
  Subtraction is conditional on sign of remainder
Faster dividers generate multiple quotient bits per step
  Still require multiple steps

## Slide 37: Fixed-point representation

## Slide 38: Fixed-point introduction
Real (fractional) numbers may not be represented with integer numbers.
    integer a,b;
    a = 1.5;
    b = a + a; // b = ?
Fixed-point representation allows real number representation with limited precision.
  Qm.n representation
    m  number of bits for representing integer part.
    n  number of bits for representing fractional part.
    Range
    Resolution is

## Slide 39: Fixed-point
Fixed-point representation is suitable for embedded applications requiring limited degree of fractional precision.
  DOOM (1993 videogame) originally used a Q16.16 format for all non-integer operations https://doomwiki.org/wiki/Fixed_point
What about high-precision applications?

## Slide 40: Fixed-point limitations
Example:
  Consider Avogadro’s number:
    How many bits would you need to represent Avogadro’s number?
79
  What about a very small number such as Planck’s constant:
    How many bits (fractional fixed-point) would you need to represent Planck’s constant?
  We would need at least bits for representing both numbers.
    Not feasible, waste of resources.
    What if need even smaller or larger numbers?

## Slide 41: Floating-point representation

## Slide 42: Floating-point
Scientific notation
  A single digit to the left of the decimal point
    Sign
    Mantissa/significant
    Exponent
Normalized scientific notation
  Absolute value of integer part is in the range
   1
Binary numbers may also be represented in scientific notation
normalized
not normalized
normalized
not normalized

## Slide 43: Floating-point
As the name suggest, binary point is not fixed.
Representation for non-integral numbers
  Including very small and very large numbers
  For simplicity, we’ll show the exponent in decimal.
Programming languages refer to this representation as float and double types.

## Slide 44: Floating-point standard
Defined by IEEE Std 754-1985
Developed in response to divergence of representations
  Portability issues for scientific code
Now almost universally adopted
Two representations
  Single precision (32-bit)
  Double precision (64-bit)
Simplifies exchange of data, arithmetic and increases accuracy.

## Slide 45: IEEE Floating-point format
sign: (0  non-negative, 1  negative)
Significand:
Normalized significand:
exponent = actual exponent + bias
  Ensures exponent is unsigned
  Single: bias = 127
  Double: bias = 1023
sign
exponent
mantissa
single: 8 bits double: 11 bits
single: 23 bits double: 52 bits
1 bit
Implicit 1

## Slide 46: IEEE Floating-point format
First example: 0.5 to single-precision floating-point
  =
  For simplification, we are using decimal notation for the exponent
  From this, we can gather the following information:
    Sign: 0
    Mantissa: 0 (normalized)
    Actual exponent: -1
  Everything together:
    Adjusted exponent= or
    Normalized floating-point:
sign
exponent
mantissa
single: 8 bits double: 11 bits
single: 23 bits double: 52 bits
1 bit

## Slide 47: IEEE Floating-point format
First example: 0.5 to single-precision floating-point
What about 0.5 in double-precision?
  0000000000000000000000000000000000000000000000000000
sign
exponent
mantissa
single: 8 bits double: 11 bits
single: 23 bits double: 52 bits
1 bit
This 1 is not actually required here

## Slide 48: Floating-point example
Represent –0.75
  –0.75 = (–1)1 × 1.12 × 2–1
  sign = 1
  mantissa = 1000…002
  exponent = –1 + bias
    Single: –1 + 127 = 126 = 011111102
    Double: –1 + 1023 = 1022 = 011111111102
Single: 1011111101000…00
Double: 1011111111101000…00

## Slide 49: Floating-point example
What number is represented by the single-precision float
11000000101000000000000000000000
  sign = 1
  exponent = 100000012 = 129
  mantissa = 01000…002
1 (1.012) 2(129 – 127)
  22
sign
exponent
mantissa
single: 8 bits double: 11 bits
single: 23 bits double: 52 bits
1 bit
Remember that this 1 is always implied!

## Slide 50: Single precision range
Exponents 00000000 and 11111111 reserved
Smallest value
exponent: 00000001  actual exponent = 1 – 127 = –126
Fraction: 000…00  significand = 1.0
±1.0 × 2–126 ≈ ±1.2 × 10–38
Largest value
exponent: 11111110  actual exponent = 254 – 127 = +127
Fraction: 111…11  significand ≈ 2.0
±2.0 × 2+127 ≈ ±3.4 × 10+38

## Slide 51: Double precision range
Exponents 00000000000 and 11111111111 reserved
Smallest value
Exponent: 00000000001  actual exponent = 1 – 1023 = –1022
Fraction: 000…00  significand = 1.0
±1.0 × 2–1022 ≈ ±2.2 × 10–308
Largest value
exponent: 11111111110  actual exponent = 2046 – 1023 = +1023
Fraction: 111…11  significand ≈ 2.0
±2.0 × 2+1023 ≈ ±1.8 × 10+308

## Slide 52: Floating-point precision
Relative precision
  Single: approx. decimal digits
  Double: approx. decimal digits

## Slide 53: Floating-point special representation
Denormal numbers
  In normalised numbers, significand have an implicit leading 1
  Denormal numbers have a leading 0 in the significand.
  Biased exponent is 0.
  These numbers allow to represent numbers smaller than the smaller normalised number, as well as special representation such as and NaN ).

## Slide 54: Denormal numbers
Smaller than normal numbers.
Zero
  sign = 0,1
  biased exponent = 0
  mantissa = 0
Two representations of 0.0!

## Slide 55: Denormalized numbers
Smallest denormalized value
Single precision:
Single precision: 〖±2^(−23)×2^(−126)≈1.4×10〗^(−45)
Largest denormalized value
Single precision:
Single precision: 〖±(1−2^(−23) )×2^(−126)≈±1.17×10〗^(−38)
Double precision:
Double precision: 〖±2^(−52)×2^(−1022)≈4.9×10〗^(−324)
Double precision:
Double precision: 〖±(1−2^(−52) )×2^(−1022)≈±2.22×10〗^(−308)
Smallest denormalized value
Largest denormalized value

## Slide 56: Infinities and NaNs
Exponent = 111...1, mantissa = 000...0
  Can be used in subsequent calculations, avoiding need for overflow check
Exponent = 111...1, mantissa ≠ 000...0
  Not-a-Number (NaN)
  Indicates illegal or undefined result
    e.g., 0.0 / 0.0
  Can be used in subsequent calculations

## Slide 57: Floating-point special formats summary

## Slide 58: Floating-point addition

## Slide 59: Floating-point addition
1. Align decimal points
Shift number with smaller exponent
9.999 × 101 + 0.016 × 101
9.999 × 101 + 0.016 × 101 = 10.015 × 101
3. Normalize result & check for over/underflow
1.0015 × 102
4. Round and renormalize if necessary
1.002 × 102
2. Add significands
Consider a decimal example
Rounding up to 3 decimal places

## Slide 60: Floating-point addition
Consider a floating-point example
  or (0.5+-0.4375)
1. Align decimal points
Shift number with smaller exponent
〖1.000〗_2×2^(−1)+ −〖0.1110〗_2×2^(−1)
1.0002 × 2^(−1) + –0.1112 × 2^(−1) = 0.0012 × 2^(−1)
3. Normalize result & check for over/underflow
〖1.0〗_2×2^(−4)
4. Round and renormalize if necessary
〖1.0〗_2×2^(−4)=0.0625
2. Add significands
1. Align decimal points
3. Normalize result & check for over/underflow
4. Round and renormalize if necessary
2. Add significands

## Slide 61: Floating-point adder hardware
Much more complex than integer adder.
Doing it in one clock cycle would take too long.
  Much longer than integer operations.
  Slower clock would penalize all instructions.
Floating-point adder usually takes several cycles
  Can be pipelined

## Slide 62: Floating-point adder hardware
Step 1
Step 2
Step 3
Step 4

## Slide 63: Floating-point adder hardware
Step 1
Step 2
Step 3
Step 4

## Slide 64: Floating-point adder hardware
Step 1
Step 2
Step 3
Step 4

## Slide 65: Floating-point adder hardware
Step 1
Step 2
Step 3
Step 4

## Slide 66: Floating-point adder hardware
Step 1
Step 2
Step 3
Step 4

## Slide 67: Floating-point adder hardware
Step 1
Step 2
Step 3
Step 4

## Slide 68: Floating-point adder hardware
Step 1
Step 2
Step 3
Step 4

## Slide 69: Floating-point multiplication

## Slide 70: Floating-point multiplication
Consider a decimal example
1.110 × 1010 × 9.200 × 10^(−5)
1. Add exponents
For biased exponents, subtract bias from sum
New exponent = 10 + –5 = 5
2. Multiply significands
1.110 × 9.200 = 10.212  10.212 × 105
3. Normalize result & check for over/underflow
1.0212 × 106
4. Round and renormalize if necessary
1.021 × 106
5. Determine sign of result from signs of operands
+1.021 × 106
Consider a decimal example
1. Add exponents
For biased exponents, subtract bias from sum
New exponent = 10 + –5 = 5
2. Multiply significands
3. Normalize result & check for over/underflow
4. Round and renormalize if necessary
5. Determine sign of result from signs of operands

## Slide 71: Floating-point multiplication
Consider a floating-point example
in decimal, or
−14.25 ×3.125 in decimal, or
1. Add exponents
Unbiased: 3 + 1 = 4
Biased: (3 + 127) + (1 + 127)
Biased: (3 + 127) + (1 + 127)−127
2. Multiply significands
−1.110012×1.10012
3. Normalize result & check for over/underflow
with no over/underflow
1.01100100012×2^5 with no over/underflow
4. Round and renormalize if necessary
(no change)
1.01100100012×2^5(no change)
5. Determine sign of result from signs of operands
–1.01100100012×2^5= –44.53125
= 〖10.110010001〗_2
−1.110012×2^3×1.10012×2^1
= 4 + 254 – 127 = 4 + 127
 10.1100100012×2^4
Consider a floating-point example
1. Add exponents
2. Multiply significands
3. Normalize result & check for over/underflow
4. Round and renormalize if necessary
5. Determine sign of result from signs of operands

## Slide 72: Floating-point multiplication
What’s the floating-point of the previous result?
  sign = 1
  exponent
    Single precision:
    Double precision:
  mantissa =
  Floating point representation:
Single precision:
  Double precision:

## Slide 73: Floating-point arithmetic hardware
Floating-point multiplier is of similar complexity to floating-point adder.
  But uses a multiplier for significands instead of an adder.
Floating-point arithmetic hardware usually does
  Addition, subtraction, multiplication, division, reciprocal, square-root.
  Floating-point  integer conversion
Operations usually takes several cycles
  Can be pipelined

## Slide 74: Floating-point rounding

## Slide 75: Floating-point rounding
Let’s try to represent in floating-point.
  Represent in binary
    Integer part is 0
    Fractional part is:
    This sequences repeats infinite times!
    0.1 is not a machine number, which means, it may not be exactly represented in a computing system.

## Slide 76: Floating-point rounding
Our floating-point representation will have to be as close as possible to
Remember that mantissa is 23 and 52 bits for single- and double-precision, respectively.
IEEE employs rounding.
  If first extra bit is 1, we add 1 to the rest of the mantissa bits – This is rounding up
  If first extra bit is 0, we drop all extra bits – This is rounding down.
  Special case if extra bits are 1000….000
    Round up if last mantissa bit is 1
    Round down if last mantissa bit is 0

## Slide 77: Floating-point rounding
Rounded normalized value:
  We rounded up for this example
(single)
Floating-point representation:
Single:
Which represents the value of
0.100000001490116119384765625
Similarly, double precision represents 0.1 as
0.1000000000000000055511151231257827021181583404541015625

## Slide 78: Floating-point rounding
In your favourite programming language try the following code using float or double data types.
Is the result TRUE or FALSE?
Problems with accuracy
  Several failures (in some cases with fatal consequences) have been reported due to numerical errors.
  http://ta.twi.tudelft.nl/users/vuik/wi211/disasters.html

## Slide 79: Concluding Remarks
Bits have no inherent meaning
  Interpretation depends on the instructions applied
Computer representations of numbers
  Finite range and precision
  Need to account for this in programs

## Slide 80: Concluding Remarks
ISAs support arithmetic operations
  Signed and unsigned integers.
  Floating-point approximation to reals.
Bounded range and precision
  Operations can overflow and underflow

## Slide 81: Arithmetic for multimedia
Graphics and media processing operates on vectors of 8-bit and 16-bit data
  Use 64-bit adder, with partitioned carry chain
    Operate on 8×8-bit, 4×16-bit, or 2×32-bit vectors
  SIMD (single-instruction, multiple-data)
Saturating operations
  On overflow, result is largest representable value
  e.g., clipping in audio, saturation in video

## Slide 82: LEGv8 Division
Two instructions:
  SDIV (signed)
  UDIV (unsigned)
Both instructions ignore overflow and division-by-zero

## Slide 83: Cortex-M0+ multiplication
MULS
  32-bit

## Slide 84: Floating-point overflow/underflow

## Slide 85: FP Instructions in LEGv8
Separate FP registers
  32 single-precision: S0, …, S31
  32 double-precision: DS0, …, D31
  Sn stored in the lower 32 bits of Dn
FP instructions operate only on FP registers
  Programs generally don’t do integer ops on FP data, or vice versa
  More registers with minimal code-size impact
FP load and store instructions
  LDURS, LDURD
  STURS, STURD

## Slide 86: FP Instructions in LEGv8
Single-precision arithmetic
  FADDS, FSUBS, FMULS, FDIVS
    e.g., FADDS S2, S4, S6
Double-precision arithmetic
  FADDD, FSUBD, FMULD, FDIVD
    e.g., FADDD D2, D4, D6
Single- and double-precision comparison
  FCMPS, FCMPD
  Sets or clears FP condition-code bits
Branch on FP condition code true or false
  B.cond

## Slide 87: FP Example: °F to °C
C code:
float f2c (float fahr) { return ((5.0/9.0)*(fahr - 32.0)); }
  fahr in S12, result in S0, literals in global memory space
Compiled LEGv8 code:
f2c:
LDURS S16, [X27,const5] // S16 = 5.0 (5.0 in memory)
LDURS S18, [X27,const9] // S18 = 9.0 (9.0 in memory)
FDIVS S16, S16, S18 // S16 = 5.0 / 9.0
LDURS S18, [X27,const32] // S18 = 32.0
FSUBS S18, S12, S18 // S18 = fahr – 32.0
FMULS S0, S16, S18 // S0 = (5/9)*(fahr – 32.0)
BR LR // return

## Slide 88: FP Example: Array Multiplication
X = X + Y × Z
  All 32 × 32 matrices, 64-bit double-precision elements
C code:
void mm (double x[][], double y[][], double z[][]) { int i, j, k; for (i = 0; i! = 32; i = i + 1) for (j = 0; j! = 32; j = j + 1) for (k = 0; k! = 32; k = k + 1) x[i][j] = x[i][j] + y[i][k] * z[k][j]; }
  Addresses of x, y, z in X0, X1, X2, and i, j, k in X19, X20, X21

## Slide 89: FP Example: Array Multiplication
LEGv8 code:
mm:...
LDI X10, 32 // X10 = 32 (row size/loop end)
LDI X19, 0 // i = 0; initialize 1st for loop
L1: LDI X20, 0 // j = 0; restart 2nd for loop
L2: LDI X21, 0 // k = 0; restart 3rd for loop
LSL X11, X19, 5 // X11 = i * 2 5 (size of row of c)
ADD X11, X11, X20 // X11 = i * size(row) + j
LSL X11, X11, 3 // X11 = byte offset of [i][j]
ADD X11, X0, X11 // X11 = byte address of c[i][j]
LDURD D4, [X11,#0] // D4 = 8 bytes of c[i][j]
L3: LSL X9, X21, 5 // X9 = k * 2 5 (size of row of b)
ADD X9, X9, X20 // X9 = k * size(row) + j
LSL X9, X9, 3 // X9 = byte offset of [k][j]
ADD X9, X2, X9 // X9 = byte address of b[k][j]
LDURD D16, [X9,#0] // D16 = 8 bytes of b[k][j]
LSL X9, X19, 5 // X9 = i * 2 5 (size of row of a)

## Slide 90: FP Example: Array Multiplication
… ADD X9, X9, X21 // X9 = i * size(row) + k
LSL X9, X9, 3 // X9 = byte offset of [i][k]
ADD X9, X1, X9 // X9 = byte address of a[i][k]
LDURD D18, [X9,#0] // D18 = 8 bytes of a[i][k]
FMULD D16, D18, D16 // D16 = a[i][k] * b[k][j]
FADDD D4, D4, D16 // f4 = c[i][j] + a[i][k] * b[k][j]
ADDI X21, X21, 1 // $k = k + 1
CMP X21, X10 // test k vs. 32
B.LT L3 // if (k < 32) go to L3
STURD D4, [X11,0] // = D4
ADDI X20, X20, #1 // $j = j + 1
CMP X20, X10 // test j vs. 32
B.LT L2 // if (j < 32) go to L2
ADDI X19, X19, #1 // $i = i + 1
CMP X19, X10 // test i vs. 32
B.LT L1 // if (i < 32) go to L1

## Slide 91: Accurate Arithmetic
IEEE Std 754 specifies additional rounding control
  Extra bits of precision (guard, round, sticky)
  Choice of rounding modes
  Allows programmer to fine-tune numerical behavior of a computation
Not all FP units implement all options
  Most programming languages and FP libraries just use defaults
Trade-off between hardware complexity, performance, and market requirements

## Slide 92: Subword Parallellism
Graphics and audio applications can take advantage of performing simultaneous operations on short vectors
  Example: 128-bit adder:
    Sixteen 8-bit adds
    Eight 16-bit adds
    Four 32-bit adds
Also called data-level parallelism, vector parallelism, or Single Instruction, Multiple Data (SIMD)

## Slide 93: ARMv8 SIMD
32 128-bit registers (V0, …, V31)
Works with integer and FP
Examples:
  16 8-bit integer adds:
  ADD V1.16B, V2.16B, V3.16B
  4 32-bit FP adds:
  FADD V1.4S, V2.4S, V3.4S

## Slide 94: Other ARMv8 Features
245 SIMD instructions, including:
  Square root
  Fused multiply-add, multiply-subtract
  Convertion and scalar and vector round-to-integral
  Structured (strided) vector load/stores
  Saturating arithmetic

## Slide 95: x86 FP Architecture
Originally based on 8087 FP coprocessor
  8 × 80-bit extended-precision registers
  Used as a push-down stack
  Registers indexed from TOS: ST(0), ST(1), …
FP values are 32-bit or 64 in memory
  Converted on load/store of memory operand
  Integer operands can also be converted on load/store
Very difficult to generate and optimize code
  Result: poor FP performance

## Slide 96: x86 FP Instructions
Optional variations
  I: integer operand
  P: pop operand from stack
  R: reverse operand order
  But not all combinations allowed
Data transfer | Arithmetic | Compare | Transcendental
FILD mem/ST(i) FISTP mem/ST(i) FLDPI FLD1 FLDZ | FIADDP mem/ST(i) FISUBRP mem/ST(i) FIMULP mem/ST(i) FIDIVRP mem/ST(i) FSQRT FABS FRNDINT | FICOMP FIUCOMP FSTSW AX/mem | FPATAN F2XMI FCOS FPTAN FPREM FPSIN FYL2X

## Slide 97: Streaming SIMD Extension 2 (SSE2)
Adds 4 × 128-bit registers
  Extended to 8 registers in AMD64/EM64T
Can be used for multiple FP operands
  2 × 64-bit double precision
  4 × 32-bit double precision
  Instructions operate on them simultaneously
    Single-Instruction Multiple-Data

## Slide 98: Matrix Multiply
Unoptimized code:
1. void dgemm (int n, double* A, double* B, double* C)
2. {
3. for (int i = 0; i < n; ++i)
4. for (int j = 0; j < n; ++j)
5. {
6. double cij = C[i+j*n]; /* cij = C[i][j] */
7. for(int k = 0; k < n; k++ )
8. cij += A[i+k*n] * B[k+j*n]; /* cij += A[i][k]*B[k][j] */
9. C[i+j*n] = cij; /* C[i][j] = cij */
10. }
11. }

## Slide 99: Matrix Multiply
x86 assembly code:
1. vmovsd (%r10),%xmm0 # Load 1 element of C into %xmm0
2. mov %rsi,%rcx # register %rcx = %rsi
3. xor %eax,%eax # register %eax = 0
4. vmovsd (%rcx),%xmm1 # Load 1 element of B into %xmm1
5. add %r9,%rcx # register %rcx = %rcx + %r9
6. vmulsd (%r8,%rax,8),%xmm1,%xmm1 # Multiply %xmm1, element of A
7. add $0x1,%rax # register %rax = %rax + 1
8. cmp %eax,%edi # compare %eax to %edi
9. vaddsd %xmm1,%xmm0,%xmm0 # Add %xmm1, %xmm0
10. jg 30 <dgemm+0x30> # jump if %eax > %edi
11. add $0x1,%r11d # register %r11 = %r11 + 1
12. vmovsd %xmm0,(%r10) # Store %xmm0 into C element

## Slide 100: Matrix Multiply
Optimized C code:
1. #include <x86intrin.h>
2. void dgemm (int n, double* A, double* B, double* C)
3. {
4. for ( int i = 0; i < n; i+=4 )
5. for ( int j = 0; j < n; j++ ) {
6. __m256d c0 = _mm256_load_pd(C+i+j*n); /* c0 = C[i][j] */
7. for( int k = 0; k < n; k++ )
8. c0 = _mm256_add_pd(c0, /* c0 += A[i][k]*B[k][j] */
9. _mm256_mul_pd(_mm256_load_pd(A+i+k*n),
10. _mm256_broadcast_sd(B+k+j*n)));
11. _mm256_store_pd(C+i+j*n, c0); /* C[i][j] = c0 */
12. }
13. }

## Slide 101: Matrix Multiply
Optimized x86 assembly code:
1. vmovapd (%r11),%ymm0 # Load 4 elements of C into %ymm0
2. mov %rbx,%rcx # register %rcx = %rbx
3. xor %eax,%eax # register %eax = 0
4. vbroadcastsd (%rax,%r8,1),%ymm1 # Make 4 copies of B element
5. add $0x8,%rax # register %rax = %rax + 8
6. vmulpd (%rcx),%ymm1,%ymm1 # Parallel mul %ymm1,4 A elements
7. add %r9,%rcx # register %rcx = %rcx + %r9
8. cmp %r10,%rax # compare %r10 to %rax
9. vaddpd %ymm1,%ymm0,%ymm0 # Parallel add %ymm1, %ymm0
10. jne 50 <dgemm+0x50> # jump if not %r10 != %rax
11. add $0x1,%esi # register % esi = % esi + 1
12. vmovapd %ymm0,(%r11) # Store %ymm0 into 4 C elements

## Slide 102: Right Shift and Division
Left shift by i places multiplies an integer by 2i
Right shift divides by 2i?
  Only for unsigned integers
For signed integers
  Arithmetic right shift: replicate the sign bit
  e.g., –5 / 4
    111110112 >> 2 = 111111102 = –2
    Rounds toward –∞
  c.f. 111110112 >>> 2 = 001111102 = +62

## Slide 103: Associativity
Parallel programs may interleave operations in unexpected orders
  Assumptions of associativity may fail
Need to validate parallel programs under varying degrees of parallelism

## Slide 104: Who Cares About FP Accuracy?
Important for scientific code
  But for everyday consumer use?
    “My bank balance is out by 0.0002¢!” 
The Intel Pentium FDIV bug
  The market expects accuracy
  See Colwell, The Pentium Chronicles