## Slide 1: TE2003B SoC Design: Computer organisation & architecture Pipeline

## Slide 2: References
The following material has been adopted and adapted from
Patterson, D. A., Hennessy, J. L., Computer Organization and design: The hardware/software interface – ARM edition, Morgan Kaufmann, 2017.
S. L. Harris and D. M. Harris, Digital design and computer architecture - ARM edition, Morgan Kaufmann, 2016.
J. Yiu, The definitive guide to ARM Cortex-M0 and Cortex-M0+ processors, Second edition, Elsevier, 2015.

## Slide 3: Background
Performance Background
Clock frequency in ICs is determined by the longest propagation delay.
Propagation delay is the time it takes for a signal to propagate from
  An input to a flip-flop
  A flip-flop to an output
  A flip-flop to another flip-flop
Notes: Isaac Pérez Andrade
5 November 2020
TE2031 – MIPS design
3

## Slide 4: Propagation delay
Clock period should be larger than largest propagation delay
  Tc > tpd

## Slide 5: Critical path
Critical path is the longest propagation delay in a circuit.
  It determines the minimum clock period of a circuit.
Which is the critical path in the following example?

## Slide 6: Critical path
Performance Background
Which is the critical path in this simplified microprocessor block diagram?
  Which type of instruction takes the longest to execute?
Notes: Isaac Pérez Andrade
5 November 2020
TE2031 – MIPS design
6

## Slide 7: Critical path
Performance Issues
LDR (load) instruction.
PC  Instruction memory  register file  mux  ALU  data memory  mux  register file
Notes: Isaac Pérez Andrade
5 November 2020
TE2031 – MIPS design
7

## Slide 8: Critical path
This critical path limits the clock frequency and the number of instructions per second that we could theoretically perform.
For example, if LDR instruction takes 10 ns to execute, what’s the maximum clock frequency we can operate?

## Slide 9: Critical path
What if we are required to run at a faster clock frequency?
  For example, our processor must operate at 500 MHz or nobody would ever buy it!
We could try to reduce the length of the critical path.
  Split the critical path into smaller logic chunks.
  Include flip-flops in the boundary of each new logic chunk.

## Slide 10: Splitting the critical path
We could split our single-cycle microprocessor execution into different stages.

## Slide 11: Splitting the critical path
This is the principle behind pipelining.

## Slide 12: Pipelining basics
Pipelining consist in breaking down a single task into several stages.

## Slide 13: Pipelining basics
Task from A to B takes the same time in both cases. What’s the advantage?

## Slide 14: Pipeline basics
We can now perform tasks in parallel!

## Slide 15: Pipeline analogy
Assume you work in a laundry shop.
You divide your job into the following stages.
  Wash (stage1)
  Dry (stage2)
  Fold (stage3)
  Store (stage4)
Assume each stage takes 30 minutes to complete.
How low would it take you to complete a single laundry task?

## Slide 16: Pipeline analogy
30min x 4 stages = 2 hours
What about 4 laundry tasks?
What about 1000 laundry tasks?

## Slide 17: Pipeline analogy
Improving our laundry efficiency.
  Start a new load right after the washing machine becomes available.
  Dry first load and wash second load at the same time.
  Fold first load, dry second load and wash third load at the same time
  Continue with this principle until you complete all four loads

## Slide 18: Pipeline analogy
4 loads now take 3.5 hours, compared to 8 hours in a sequential scheme.

## Slide 19: Pipeline speedup
How can we measure the performance improvement?
Four loads:
Speedup = 8/3.5 = 2.28
We are doing our job 2.3 times faster!
What about infinite number of loads?
Full pipeline: All resources are used at the same time
Wind-down time
Start-up time

## Slide 20: Pipeline speedup
Speedup with an infinite number of laundry loads.
Speedup is directly determined by the number of pipeline stages

## Slide 21: Pipeline speedup
Speedup for an infinite number of laundry loads
Full pipeline
Wind-down time
Start-up time

## Slide 22: Cortex-M0+ pipeline
Cortex-M0+ implements a two-stage pipeline.
We will focus on a more general five-stage pipeline

## Slide 23: ARM pipeline
ARM pipeline. Five instruction cycle stages, one step per stage.
  IF: Instruction fetch from memory
  ID: Instruction decode & register read
  EX: Execute operation or calculate address
  MEM: Access memory operand
  WB: Write result back to register

## Slide 24: Pipeline performance
Assume time for stages is
  100ps for register read or write
  200ps for other stages
Compare pipelined datapath with single-cycle datapath
Instr | Fetch | Decode | Execute | Memory access | Write back | Total
LDR | 200 ps | 100 ps | 200 ps | 200 ps | 100 ps | 800 ps
STR | 200 ps | 100 ps | 200 ps | 200 ps |  | 700 ps
R-Type | 200 ps | 100 ps | 200 ps |  | 100 ps | 600 ps
CBZ | 200 ps | 100 ps | 200 ps |  |  | 500 ps

## Slide 25: Pipeline performance
Instr | Fetch | Decode | Execute | Memory access | Write back | Total
LDR | 200 ps | 100 ps | 200 ps | 200 ps | 100 ps | 800 ps
STR | 200 ps | 100 ps | 200 ps | 200 ps |  | 700 ps
R-Type | 200 ps | 100 ps | 200 ps |  | 100 ps | 600 ps
CBZ | 200 ps | 100 ps | 200 ps |  |  | 500 ps

## Slide 26: Pipeline performance
What’s the critical path?
Single-cycle (Tc= 800ps)  1 LDR takes 800 ps
Pipelined (Tc= 200ps)  1 LDR takes 1000 ps
What’s the critical path?

## Slide 27: Pipeline speedup
Pipeline increases throughput.
  Throughput. Number of tasks performed in a given time.
  Instruction Level Parallelism (ILP).
Pipeline does not improve (reduce) instruction latency. In fact, instruction latency is usually increased.
  Latency. Required time for completing a task.

## Slide 28: Pipelining and ISA design
ARM ISA designed for pipelining
  All instructions are 32-bits
    Easier to fetch and decode in one cycle
    Compared to Intel’s x86 ISA using between 1- to 17-byte instructions.
  Few and regular instruction formats
    Can decode and read registers in one step
  Load/store addressing
    Can calculate address in 3rd stage, access memory in 4th stage
  Alignment of memory operands
    Memory access takes only one cycle

## Slide 29: Pipeline hazards

## Slide 30: Hazards
Situations that prevent starting the next instruction in the next cycle.
Structure hazards
  A required resource is busy
Data hazard
  Need to wait for previous instruction to complete its data read/write
Control hazard
  Deciding on control action depends on previous instruction

## Slide 31: Structure hazards
Hardware cannot support the combination of instructions in the same clock cycle.
Conflict for use of a resource.
  We require to use the dryer for two different sets of clothes exactly at the same time.
ARM pipeline with a single memory
  Load/store requires data access
  Instruction fetch would have to stall for that cycle
    Would cause a pipeline “bubble”
Hence, pipelined datapaths require separate instruction/data memories
  Or separate instruction/data caches

## Slide 32: Data hazards
An instruction depends on completion of data access by a previous instruction
ADD x1, x2, x3
SUB x4, x1, x5
We can’t go back in time!

## Slide 33: Data hazards
An instruction depends on completion of data access by a previous instruction
ADD x1, x2, x3
SUB x4, x1, x5
Instead of going back in time, we must stall (stop) the execution of instructions until we complete write back on first instruction

## Slide 34: Data hazards
Compiler might detect this data dependency and insert bubbles (NOP instructions).
ADD x1, x2, x3
NOP
NOP
SUB x4, x1, x5
NOP instructions do not do anything.
  Used for creating pipeline bubbles.

## Slide 35: Data hazards
Load instruction
LDUR X1, [x2, #0]
SUB X4, X1, X5

## Slide 36: Data hazards – forwarding (aka bypassing)
Forwarding tries to mitigate bubbles due to data hazards
ADD x1, x2, x3
SUB x4, x1, x5
Instead of waiting to a write back to occur, we take the required data directly from the execute stage.

## Slide 37: Data hazards - forwarding (aka bypassing)
Use result when it is computed
  Don’t wait for it to be stored in a register
  Requires extra connections in the datapath

## Slide 38: Data hazards
Can’t always avoid stalls by forwarding
  If value not computed when needed
  Can’t forward backward in time!

## Slide 39: Code scheduling to avoid stalls
Reorder code to avoid use of load result in the next instruction
A = B + E;
C = B + F;
B = Mem[0]; E = Mem[4]; F = Mem[8]
LDR X1, [X0,#0] ; load B
LDR X2, [X0,#4] ; load E
ADD X3, X1, X2 ; A=B+E
STR X3, [X0,#40]; store A
LDR X4, [X0,#8] ; load F
ADD X5, X1, X4 ; C=B+F
STR X5, [X0,#44]; store C
stall
stall
LDR X1, [X0,#0]
LDR X2, [X0,#4]
LDR X4, [X0,#8]
ADD X3, X1, X2
STR X3, [X0,#40]
ADD X5, X1, X4
STR X5, [X0,#44]
11 cycles
13 cycles

## Slide 40: Control hazards
Branch determines flow of control.
  Fetching next instruction depends on branch outcome.
  Pipeline can’t always fetch correct instruction
    Still working on ID stage of branch.
  Need to compare registers and compute target early in the pipeline.
  Add hardware to do it in ID stage

## Slide 41: Control hazards
if(a==0)
  b = c + d
  else
  b = c - d
Example 1. Assume a != 0
  CMP a, #0x00 ; Compare a==0
  BEQ if_label ; Branch if a==0
  else_label
  SUB b, c, d ; else = Branch not taken
  ; b = c - d
  :
  if_label ; if = Branch taken
  ADD b, c, d ; b = c + d

## Slide 42: Control hazards
if(a==0)
  b = c + d
  else
  b = c - d
Example 2. Assume a == 0
  CMP a, #0x00 ; Compare a==0
  BEQ if_label ; Branch if a==0
  else_label
  SUB b, c, d ; else = Branch not taken
  ; b = c - d
  :
  if_label ; if = Branch taken
  ADD b, c, d ; b = c + d

## Slide 43: Control hazards
Example 1. a != 0: Branch not taken
  Order of instructions is not modified
  Instructions already in pipeline might continue to execute.
CMP a, #0x00
BEQ if_label
SUB b, c, d
AND e, f, g

## Slide 44: Control hazards
Example 2. a == 0: Branch taken
  Order of instructions is modified
  Instructions already in pipeline will have to be discarded.
  Pipeline will have to be started again with a penalty due to wasted instructions
CMP a, #0x00
BEQ if_label
SUB b, c, d
AND e, f, g
ADD b, c, d

## Slide 45: Stall on branch
Wait until branch outcome determined before fetching next instruction
CMP a, #0x00
BEQ if_label
SUB b, c, d
AND e, f, g

## Slide 46: Branch prediction
Longer pipelines can’t readily determine branch outcome early
  Stall penalty becomes unacceptable
Predict outcome of branch
  Only stall if prediction is wrong
In ARM pipeline
  Can predict branches not taken
  Fetch instruction after branch, with no delay

## Slide 47: More-realistic branch prediction
Static branch prediction
  Based on typical branch behavior
  Example: loop and if-statement branches
    Predict backward branches taken
    Predict forward branches not taken
Dynamic branch prediction
  Hardware measures actual branch behavior
    e.g., record recent history of each branch
  Assume future behavior will continue the trend
    When wrong, stall while re-fetching, and update history

## Slide 48: Pipeline uA

## Slide 49: Pipeline summary
Pipelining improves performance by increasing instruction throughput.
  Executes multiple instructions in parallel.
  Each instruction has the same (or worse) latency.
Subject to hazards.
  Structure, data, control.
Instruction set design affects complexity of pipeline implementation.

## Slide 50: ARMv6-M Pipelined Datapath
§4.6 Pipelined Datapath and Control
WB
MEM
Right-to-left flow leads to hazards

## Slide 51: Pipeline registers
Need registers between stages
  To hold information produced in previous cycle

## Slide 52: Pipeline Operation
Cycle-by-cycle flow of instructions through the pipelined datapath
  “Single-clock-cycle” pipeline diagram
    Shows pipeline usage in a single cycle
    Highlight resources used
  c.f. “multi-clock-cycle” diagram
    Graph of operation over time
We’ll look at “single-clock-cycle” diagrams for load & store

## Slide 53: IF for Load, Store, …

## Slide 54: ID for Load, Store, …

## Slide 55: EX for Load

## Slide 56: MEM for Load

## Slide 57: WB for Load
Wrong register number

## Slide 58: Corrected Datapath for Load

## Slide 59: EX for Store

## Slide 60: MEM for Store

## Slide 61: WB for Store

## Slide 62: Multi-Cycle Pipeline Diagram
Form showing resource usage

## Slide 63: Multi-Cycle Pipeline Diagram
Traditional form

## Slide 64: Single-Cycle Pipeline Diagram
State of pipeline in a given cycle

## Slide 65: Pipelined Control (Simplified)

## Slide 66: Pipelined Control
Control signals derived from instruction
  As in single-cycle implementation

## Slide 67: Pipelined Control

## Slide 68: Data Hazards in ALU Instructions
Consider this sequence:
  SUB X2, X1,X3 AND X12,X2,X5 OR X13,X6,X2 ADD X14,X2,X2 STUR X15,[X2,#100]
We can resolve hazards with forwarding
  How do we detect when to forward?
§4.7 Data Hazards: Forwarding vs. Stalling

## Slide 69: Dependencies & Forwarding

## Slide 70: Detecting the Need to Forward
Pass register numbers along pipeline
  e.g., ID/EX.RegisterRs = register number for Rs sitting in ID/EX pipeline register
ALU operand register numbers in EX stage are given by
  ID/EX.RegisterRn1, ID/EX.RegisterRm2
Data hazards when
  1a. EX/MEM.RegisterRd = ID/EX.RegisterRn1
  1b. EX/MEM.RegisterRd = ID/EX.RegisterRm2
  2a. MEM/WB.RegisterRd = ID/EX.RegisterRn1
  2b. MEM/WB.RegisterRd = ID/EX.RegisterRm2
Fwd from EX/MEM pipeline reg
Fwd from MEM/WB pipeline reg

## Slide 71: Detecting the Need to Forward
But only if forwarding instruction will write to a register!
  EX/MEM.RegWrite, MEM/WB.RegWrite
And only if Rd for that instruction is not XZR
  EX/MEM.RegisterRd ≠ 31, MEM/WB.RegisterRd ≠ 31

## Slide 72: Forwarding Paths

## Slide 73: Forwarding Conditions
Mux control | Source | Explanation
ForwardA = 00 | ID/EX | The first ALU operand comes from the register file.
ForwardA = 10 | EX/MEM | The first ALU operand is forwarded from the prior ALU result.
ForwardA = 01 | MEM/WB | The first ALU operand is forwarded from data memory or an earlier ALU result.
ForwardB = 00 | ID/EX | The second ALU operand comes from the register file.
ForwardB = 10 | EX/MEM | The second ALU operand is forwarded from the prior ALU result.
ForwardB = 01 | MEM/WB | The second ALU operand is forwarded from data memory or an earlier ALU result.

## Slide 74: Double Data Hazard
Consider the sequence:
  add X1,X1,X2 add X1,X1,X3 add X1,X1,X4
Both hazards occur
  Want to use the most recent
Revise MEM hazard condition
  Only fwd if EX hazard condition isn’t true

## Slide 75: Revised Forwarding Condition
MEM hazard
  if (MEM/WB.RegWrite
  and (MEM/WB.RegisterRd ≠ 31)
  and not(EX/MEM.RegWrite and (EX/MEM.RegisterRd ≠ 31)
  and (EX/MEM.RegisterRd ≠ ID/EX.RegisterRn1))
  and (MEM/WB.RegisterRd = ID/EX.RegisterRn1)) ForwardA = 01
  if (MEM/WB.RegWrite
  and (MEM/WB.RegisterRd ≠ 31)
  and not(EX/MEM.RegWrite and (EX/MEM.RegisterRd ≠ 31)
  and (EX/MEM.RegisterRd ≠ ID/EX.RegisterRm2))
  and (MEM/WB.RegisterRd = ID/EX.RegisterRm2)) ForwardB = 01

## Slide 76: Datapath with Forwarding

## Slide 77: Load-Use Hazard Detection
Check when using instruction is decoded in ID stage
ALU operand register numbers in ID stage are given by
  IF/ID.RegisterRn1, IF/ID.RegisterRm2
Load-use hazard when
  ID/EX.MemRead and ((ID/EX.RegisterRd = IF/ID.RegisterRn1) or (ID/EX.RegisterRd = IF/ID.RegisterRm1))
If detected, stall and insert bubble

## Slide 78: How to Stall the Pipeline
Force control values in ID/EX register to 0
  EX, MEM and WB do nop (no-operation)
Prevent update of PC and IF/ID register
  Using instruction is decoded again
  Following instruction is fetched again
  1-cycle stall allows MEM to read data for LDUI
    Can subsequently forward to EX stage

## Slide 79: Load-Use Data Hazard
Stall inserted here

## Slide 80: Datapath with Hazard Detection

## Slide 81: Stalls and Performance
Stalls reduce performance
  But are required to get correct results
Compiler can arrange code to avoid hazards and stalls
  Requires knowledge of the pipeline structure
The BIG Picture

## Slide 82: Branch Hazards
If branch outcome determined in MEM
§4.8 Control Hazards
PC
Flush these instructions
(Set control values to 0)

## Slide 83: Reducing Branch Delay
Move hardware to determine outcome to ID stage
  Target address adder
  Register comparator
Example: branch taken
  36: SUB X10, X4, X8 40: CBZ X1, X3, 8 44: AND X12, X2, X5 48: ORR X13, X2, X6 52: ADD X14, X4, X2 56: SUB X15, X6, X7 ... 72: LDUR X4, [X7,#50]

## Slide 84: Example: Branch Taken

## Slide 85: Example: Branch Taken

## Slide 86: Dynamic Branch Prediction
In deeper and superscalar pipelines, branch penalty is more significant
Use dynamic prediction
  Branch prediction buffer (aka branch history table)
  Indexed by recent branch instruction addresses
  Stores outcome (taken/not taken)
  To execute a branch
    Check table, expect the same outcome
    Start fetching from fall-through or target
    If wrong, flush pipeline and flip prediction

## Slide 87: 1-Bit Predictor: Shortcoming
Inner loop branches mispredicted twice!
outer: … … inner: …
…
CBZ …, …, inner … CBZ …, …, outer
  Mispredict as taken on last iteration of inner loop
  Then mispredict as not taken on first iteration of inner loop next time around

## Slide 88: 2-Bit Predictor
Only change prediction on two successive mispredictions

## Slide 89: Calculating the Branch Target
Even with predictor, still need to calculate the target address
  1-cycle penalty for a taken branch
Branch target buffer
  Cache of target addresses
  Indexed by PC when instruction fetched
    If hit and instruction is branch predicted taken, can fetch target immediately

## Slide 90: Exceptions and Interrupts
“Unexpected” events requiring change in flow of control
  Different ISAs use the terms differently
Exception
  Arises within the CPU
    e.g., undefined opcode, overflow, syscall, …
Interrupt
  From an external I/O controller
Dealing with them without sacrificing performance is hard
§4.9 Exceptions

## Slide 91: Handling Exceptions
Save PC of offending (or interrupted) instruction
  In ARMv6-M: Exception Link Register (ELR)
Save indication of the problem
  In ARMv6-M: Exception Syndrome Rregister (ESR)
  We’ll assume 1-bit
    0 for undefined opcode, 1 for overflow

## Slide 92: An Alternate Mechanism
Vectored Interrupts
  Handler address determined by the cause
Exception vector address to be added to a vector table base register:
  Unknown Reason: 00 0000two
  Overflow: 10 1100two
  …: 11 1111two
Instructions either
  Deal with the interrupt, or
  Jump to real handler

## Slide 93: Handler Actions
Read cause, and transfer to relevant handler
Determine action required
If restartable
  Take corrective action
  use EPC to return to program
Otherwise
  Terminate program
  Report error using EPC, cause, …

## Slide 94: Exceptions in a Pipeline
Another form of control hazard
Consider overflow on add in EX stage
  ADD X1, X2, X1
  Prevent X1 from being clobbered
  Complete previous instructions
  Flush add and subsequent instructions
  Set ESR and ELR register values
  Transfer control to handler
Similar to mispredicted branch
  Use much of the same hardware

## Slide 95: Pipeline with Exceptions

## Slide 96: Exception Properties
Restartable exceptions
  Pipeline can flush the instruction
  Handler executes, then returns to the instruction
    Refetched and executed from scratch
PC saved in ELR register
  Identifies causing instruction
  Actually PC + 4 is saved
    Handler must adjust

## Slide 97: Exception Example
Exception on ADD in
  40 SUB X11, X2, X4 44 AND X12, X2, X5 48 ORR X13, X2, X6 4C ADD X1, X2, X1 50 SUB X15, X6, X7 54 LDUR X16, [X7,#100] …
Handler
  80000180 STUR X26, [X0,#1000] 80000184 STUR X27, [X0,#1008] …

## Slide 98: Exception Example

## Slide 99: Exception Example

## Slide 100: Multiple Exceptions
Pipelining overlaps multiple instructions
  Could have multiple exceptions at once
Simple approach: deal with exception from earliest instruction
  Flush subsequent instructions
  “Precise” exceptions
In complex pipelines
  Multiple instructions issued per cycle
  Out-of-order completion
  Maintaining precise exceptions is difficult!

## Slide 101: Imprecise Exceptions
Just stop pipeline and save state
  Including exception cause(s)
Let the handler work out
  Which instruction(s) had exceptions
  Which to complete or flush
    May require “manual” completion
Simplifies hardware, but more complex handler software
Not feasible for complex multiple-issue out-of-order pipelines

## Slide 102: Instruction-Level Parallelism (ILP)
Pipelining: executing multiple instructions in parallel
To increase ILP
  Deeper pipeline
    Less work per stage  shorter clock cycle
  Multiple issue
    Replicate pipeline stages  multiple pipelines
    Start multiple instructions per clock cycle
    CPI < 1, so use Instructions Per Cycle (IPC)
    E.g., 4GHz 4-way multiple-issue
      16 BIPS, peak CPI = 0.25, peak IPC = 4
    But dependencies reduce this in practice
§4.10 Parallelism via Instructions

## Slide 103: Multiple Issue
Static multiple issue
  Compiler groups instructions to be issued together
  Packages them into “issue slots”
  Compiler detects and avoids hazards
Dynamic multiple issue
  CPU examines instruction stream and chooses instructions to issue each cycle
  Compiler can help by reordering instructions
  CPU resolves hazards using advanced techniques at runtime

## Slide 104: Speculation
“Guess” what to do with an instruction
  Start operation as soon as possible
  Check whether guess was right
    If so, complete the operation
    If not, roll-back and do the right thing
Common to static and dynamic multiple issue
Examples
  Speculate on branch outcome
    Roll back if path taken is different
  Speculate on load
    Roll back if location is updated

## Slide 105: Compiler/Hardware Speculation
Compiler can reorder instructions
  e.g., move load before branch
  Can include “fix-up” instructions to recover from incorrect guess
Hardware can look ahead for instructions to execute
  Buffer results until it determines they are actually needed
  Flush buffers on incorrect speculation

## Slide 106: Speculation and Exceptions
What if exception occurs on a speculatively executed instruction?
  e.g., speculative load before null-pointer check
Static speculation
  Can add ISA support for deferring exceptions
Dynamic speculation
  Can buffer exceptions until instruction completion (which may not occur)

## Slide 107: Static Multiple Issue
Compiler groups instructions into “issue packets”
  Group of instructions that can be issued on a single cycle
  Determined by pipeline resources required
Think of an issue packet as a very long instruction
  Specifies multiple concurrent operations
   Very Long Instruction Word (VLIW)

## Slide 108: Scheduling Static Multiple Issue
Compiler must remove some/all hazards
  Reorder instructions into issue packets
  No dependencies with a packet
  Possibly some dependencies between packets
    Varies between ISAs; compiler must know!
  Pad with nop if necessary

## Slide 109: ARMv6-M with Static Dual Issue
Two-issue packets
  One ALU/branch instruction
  One load/store instruction
  64-bit aligned
    ALU/branch, then load/store
    Pad an unused instruction with nop
Address | Instruction type | Pipeline Stages |  |  |  |  |  | 
n | ALU/branch | IF | ID | EX | MEM | WB |  | 
n + 4 | Load/store | IF | ID | EX | MEM | WB |  | 
n + 8 | ALU/branch |  | IF | ID | EX | MEM | WB | 
n + 12 | Load/store |  | IF | ID | EX | MEM | WB | 
n + 16 | ALU/branch |  |  | IF | ID | EX | MEM | WB
n + 20 | Load/store |  |  | IF | ID | EX | MEM | WB

## Slide 110: ARMv6-M with Static Dual Issue

## Slide 111: Hazards in the Dual-Issue ARMv6-M
More instructions executing in parallel
EX data hazard
  Forwarding avoided stalls with single-issue
  Now can’t use ALU result in load/store in same packet
    ADD X0, X0, X1 LDUR X2, [X0,#0]
    Split into two packets, effectively a stall
Load-use hazard
  Still one cycle use latency, but now two instructions
More aggressive scheduling required

## Slide 112: Scheduling Example
Schedule this for dual-issue ARMv6-M
Loop: LDUR X0, [X20,#0] // X0=array element ADD X0, X0,X21 // add scalar in X21 STUR X0, [X20,#0] // store result SUBI X20, X20,#4 // decrement pointer CMP X20, X22 // branch $s1!=0
BGT Loop
 | ALU/branch | Load/store | cycle
Loop: | nop | LDUR X0, [X20,#0] | 1
 | SUBI X20, X20,#4 | nop | 2
 | ADD X0, X0,X21 | nop | 3
 | CMP X20, X22 | sw $t0, 4($s1) | 4
 | BGT Loop | STUR X0, [X20,#0] | 5
  IPC = 7/6 = 1.17 (c.f. peak IPC = 2)

## Slide 113: Loop Unrolling
Replicate loop body to expose more parallelism
  Reduces loop-control overhead
Use different registers per replication
  Called “register renaming”
  Avoid loop-carried “anti-dependencies”
    Store followed by a load of the same register
    Aka “name dependence”
      Reuse of a register name

## Slide 114: Loop Unrolling Example
IPC = 15/8 = 1.875
  Closer to 2, but at cost of registers and code size
 | ALU/branch | Load/store | cycle
Loop: | SUBI X20, X20,#32 | LDUR X0, [X20,#0] | 1
 | nop | LDUR X1, [X20,#24] | 2
 | ADD X0, X0, X21 | LDUR X2, [X20,#16] | 3
 | ADD X1, X1, X21 | LDUR X3, [X20,#8] | 4
 | ADD X2, X2, X21 | STUR X0, [X20,#32] | 5
 | ADD X3, X3, X21 | sw X1, [X20,#24] | 6
 | CMP X20,X22 | sw X2, [X20,#16] | 7
 | BGT Loop | sw X3, [X20,#8] | 8

## Slide 115: Dynamic Multiple Issue
“Superscalar” processors
CPU decides whether to issue 0, 1, 2, … each cycle
  Avoiding structural and data hazards
Avoids the need for compiler scheduling
  Though it may still help
  Code semantics ensured by the CPU

## Slide 116: Dynamic Pipeline Scheduling
Allow the CPU to execute instructions out of order to avoid stalls
  But commit result to registers in order
Example
  LDUR X0, [X21,#20] ADD X1, X0, X2 SUB X23,X23,X3 ANDI X5, X23,#20
  Can start sub while ADD is waiting for LDUI

## Slide 117: Dynamically Scheduled CPU
Results also sent to any waiting reservation stations
Reorders buffer for register writes
Can supply operands for issued instructions
Preserves dependencies
Hold pending operands

## Slide 118: Register Renaming
Reservation stations and reorder buffer effectively provide register renaming
On instruction issue to reservation station
  If operand is available in register file or reorder buffer
    Copied to reservation station
    No longer required in the register; can be overwritten
  If operand is not yet available
    It will be provided to the reservation station by a function unit
    Register update may not be required

## Slide 119: Speculation
Predict branch and continue issuing
  Don’t commit until branch outcome determined
Load speculation
  Avoid load and cache miss delay
    Predict the effective address
    Predict loaded value
    Load before completing outstanding stores
    Bypass stored values to load unit
  Don’t commit load until speculation cleared

## Slide 120: Why Do Dynamic Scheduling?
Why not just let the compiler schedule code?
Not all stalls are predicable
  e.g., cache misses
Can’t always schedule around branches
  Branch outcome is dynamically determined
Different implementations of an ISA have different latencies and hazards

## Slide 121: Does Multiple Issue Work?
Yes, but not as much as we’d like
Programs have real dependencies that limit ILP
Some dependencies are hard to eliminate
  e.g., pointer aliasing
Some parallelism is hard to expose
  Limited window size during instruction issue
Memory delays and limited bandwidth
  Hard to keep pipelines full
Speculation can help if done well
The BIG Picture

## Slide 122: Power Efficiency
Complexity of dynamic scheduling and speculations requires power
Multiple simpler cores may be better
Microprocessor | Year | Clock Rate | Pipeline Stages | Issue width | Out-of-order/ Speculation | Cores | Power
i486 | 1989 | 25MHz | 5 | 1 | No | 1 | 5W
Pentium | 1993 | 66MHz | 5 | 2 | No | 1 | 10W
Pentium Pro | 1997 | 200MHz | 10 | 3 | Yes | 1 | 29W
P4 Willamette | 2001 | 2000MHz | 22 | 3 | Yes | 1 | 75W
P4 Prescott | 2004 | 3600MHz | 31 | 3 | Yes | 1 | 103W
Core | 2006 | 2930MHz | 14 | 4 | Yes | 2 | 75W
UltraSparc III | 2003 | 1950MHz | 14 | 4 | No | 1 | 90W
UltraSparc T1 | 2005 | 1200MHz | 6 | 1 | No | 8 | 70W

## Slide 123: Cortex A53 and Intel i7
Processor | ARM A53 | Intel Core i7 920
Market | Personal Mobile Device | Server, cloud
Thermal design power | 100 milliWatts (1 core @ 1 GHz) | 130 Watts
Clock rate | 1.5 GHz | 2.66 GHz
Cores/Chip | 4 (configurable) | 4
Floating point? | Yes | Yes
Multiple issue? | Dynamic | Dynamic
Peak instructions/clock cycle | 2 | 4
Pipeline stages | 8 | 14
Pipeline schedule | Static in-order | Dynamic out-of-order with speculation
Branch prediction | Hybrid | 2-level
1st level caches/core | 16-64 KiB I, 16-64 KiB D | 32 KiB I, 32 KiB D
2nd level caches/core | 128-2048 KiB | 256 KiB (per core)
3rd level caches (shared) | (platform dependent) | 2-8 MB
§4.11 Real Stuff: The ARM Cortex-A8 and Intel Core i7 Pipelines

## Slide 124: ARM Cortex-A53 Pipeline

## Slide 125: ARM Cortex-A53 Performance

## Slide 126: Core i7 Pipeline

## Slide 127: Core i7 Performance

## Slide 128: Matrix Multiply
Unrolled C code
1 #include <x86intrin.h>
2 #define UNROLL (4)
3
4 void dgemm (int n, double* A, double* B, double* C)
5 {
6 for ( int i = 0; i < n; i+=UNROLL*4 )
7 for ( int j = 0; j < n; j++ ) {
8 __m256d c[4];
9 for ( int x = 0; x < UNROLL; x++ )
10 c[x] = _mm256_load_pd(C+i+x*4+j*n);
11
12 for( int k = 0; k < n; k++ )
13 {
14 __m256d b = _mm256_broadcast_sd(B+k+j*n);
15 for (int x = 0; x < UNROLL; x++)
16 c[x] = _mm256_add_pd(c[x],
17 _mm256_mul_pd(_mm256_load_pd(A+n*k+x*4+i), b));
18 }
19
20 for ( int x = 0; x < UNROLL; x++ )
21 _mm256_store_pd(C+i+x*4+j*n, c[x]);
22 }
23 }
§4.12 Instruction-Level Parallelism and Matrix Multiply

## Slide 129: Matrix Multiply
Assembly code:
1 vmovapd (%r11),%ymm4 # Load 4 elements of C into %ymm4
2 mov %rbx,%rax # register %rax = %rbx
3 xor %ecx,%ecx # register %ecx = 0
4 vmovapd 0x20(%r11),%ymm3 # Load 4 elements of C into %ymm3
5 vmovapd 0x40(%r11),%ymm2 # Load 4 elements of C into %ymm2
6 vmovapd 0x60(%r11),%ymm1 # Load 4 elements of C into %ymm1
7 vbroadcastsd (%rcx,%r9,1),%ymm0 # Make 4 copies of B element
8 add $0x8,%rcx # register %rcx = %rcx + 8
9 vmulpd (%rax),%ymm0,%ymm5 # Parallel mul %ymm1,4 A elements
10 vaddpd %ymm5,%ymm4,%ymm4 # Parallel add %ymm5, %ymm4
11 vmulpd 0x20(%rax),%ymm0,%ymm5 # Parallel mul %ymm1,4 A elements
12 vaddpd %ymm5,%ymm3,%ymm3 # Parallel add %ymm5, %ymm3
13 vmulpd 0x40(%rax),%ymm0,%ymm5 # Parallel mul %ymm1,4 A elements
14 vmulpd 0x60(%rax),%ymm0,%ymm0 # Parallel mul %ymm1,4 A elements
15 add %r8,%rax # register %rax = %rax + %r8
16 cmp %r10,%rcx # compare %r8 to %rax
17 vaddpd %ymm5,%ymm2,%ymm2 # Parallel add %ymm5, %ymm2
18 vaddpd %ymm0,%ymm1,%ymm1 # Parallel add %ymm0, %ymm1
19 jne 68 <dgemm+0x68> # jump if not %r8 != %rax
20 add $0x1,%esi # register % esi = % esi + 1
21 vmovapd %ymm4,(%r11) # Store %ymm4 into 4 C elements
22 vmovapd %ymm3,0x20(%r11) # Store %ymm3 into 4 C elements
23 vmovapd %ymm2,0x40(%r11) # Store %ymm2 into 4 C elements
24 vmovapd %ymm1,0x60(%r11) # Store %ymm1 into 4 C elements
§4.12 Instruction-Level Parallelism and Matrix Multiply

## Slide 130: Performance Impact

## Slide 131: Fallacies
Pipelining is easy (!)
  The basic idea is easy
  The devil is in the details
    e.g., detecting data hazards
Pipelining is independent of technology
  So why haven’t we always done pipelining?
  More transistors make more advanced techniques feasible
  Pipeline-related ISA design needs to take account of technology trends
    e.g., predicated instructions
§4.14 Fallacies and Pitfalls

## Slide 132: Pitfalls
Poor ISA design can make pipelining harder
  e.g., complex instruction sets (VAX, IA-32)
    Significant overhead to make pipelining work
    IA-32 micro-op approach
  e.g., complex addressing modes
    Register update side effects, memory indirection
  e.g., delayed branches
    Advanced pipelines have long delay slots

## Slide 133: Concluding Remarks
ISA influences design of datapath and control
Datapath and control influence design of ISA
Pipelining improves instruction throughput using parallelism
  More instructions completed per second
  Latency for each instruction not reduced
Hazards: structural, data, control
Multiple issue and dynamic scheduling (ILP)
  Dependencies limit achievable parallelism
  Complexity leads to the power wall
§4.14 Concluding Remarks