## Slide 1: TE2003B SoC Design: Computer organisation & architecture Introduction to Cortex-M0+ assembly language

## Slide 2: References
The following material has been adopted and adapted from
Patterson, D. A., Hennessy, J. L., Computer Organization and design: The hardware/software interface – ARM edition, Morgan Kaufmann, 2017.
S. L. Harris and D. M. Harris, Digital design and computer architecture - ARM edition, Morgan Kaufmann, 2016.
J. Yiu, The definitive guide to ARM Cortex-M0 and Cortex-M0+ processors, Second edition, Elsevier, 2015.

## Slide 3: Recalling abstraction
Jumping up a few levels of abstraction
  Architecture: programmer’s view of computer
    Defined by instructions & operand locations
  Microarchitecture: how to implement an architecture in hardware.

## Slide 4: From human-language to machine language
Commands in a computer’s language
  Assembly language: human-readable format of instructions
  Machine language: computer-readable format (1’s and 0’s)

## Slide 5: Why assembler language?
High-level languages provide flexibility to the programmer.
  Close to human language.
  A C program might be ported between different systems with minor modifications.
Assembly language is specific to each Instruction Set Architecture (ISA).
  We can’t simply take ARM assembly code and easily convert it to Intel assembly.

## Slide 6: Why assembly language?

## Slide 7: Assembly advantages
Time efficient.
  Fast compile times.
  Yields fast program execution.
Memory efficient.
  Program stored efficiently in system’s memory.
Efficient use of resources.
  Programmers have direct access to resources such as registers, memory, Input/Output (IO) ports, peripherals, etc.

## Slide 8: ARM’s background
Developed in the 1980’s by Advanced RISC Machines – now called ARM Holdings.
ARM does not fabricate Integrated Circuits (ICs).
ARM licenses (sells) P cores in the form of Intellectual Property (IP).
ARM architecture has several variants, which are identified as ARMvX.
  For example: Freescale’s KL25Z C (Microcontroller) is based on ARM’s Cortex-M0+ (read as M zero plus), which is based on ARMv6-M ISA.

## Slide 9: ARM’s background
Nearly 10 billion ARM processors sold/year
Almost all cell phones and tablets have multiple ARM processors
Over 75% of humans use products with an ARM processor
Used in servers, cameras, robots, cars, pinball machines,, etc.
Once you’ve learned one architecture, it’s easier to learn others

## Slide 10: ARM core families
Based on ARMv6-M ISA

## Slide 11: Cortex-M0+ instructions
Cortex-M0+ processors are not designed for heavy duty number crunching.
  No Floating-Point Unit (FPU).
  Multiplication (MUL) available, however, no division instruction available.
Designed for handling general data, IO control tasks in ultra low power and low-cost systems.
Upwards compatibility.
  Program developed for Cortex-M0+ might run without (major) changes in Cortex-M7 processors.

## Slide 12: Cortex-M0+ main characteristics
32-bit RISC processor
16 32-bit registers
  Some of these registers have a special purpose
56 instructions
  50 16-bit instructions
  6 32-bit instructions
Stack Pointer (SP)
Designed for low-power applications

## Slide 13: Cortex-M0+ instructions
ARM Cortex-M processors support the instruction set called Thumb.
Cortex-M0+ support only a subset (56) instructions.
50/56 instructions encoded in 16 bits.
6/56 instructions encoded in 32 bits.

## Slide 14: Cortex-M0+ instructions
Data processing instructions.
  Arithmetic and logic operations.
Memory access instructions.
  Read/write from/to memory.
Program flow control.
  Branches, function calls.
Exception and Operative System (OS) support.
Special registers.
Sleep operations.
Memory barriers.

## Slide 15: Cortex-M0+ registers
Figure 8: Cortex-M0+ registers
Many Thumb instructions can only access R0-R7.
Assembly code syntax allows using both upper- and lower-case letters.
R0 == r0
R13 == r13 == SP
R14 == r14 == LR
R15 == r15 == PC

## Slide 16: Cortex-M0+ memory map
16 registers are not enough for storing all the required data.
  Code (instructions, program)
  Data (user data such as variables and constants)
Cortex-M0+ provides a total of 4 GB of memory space, divided into several regions.

## Slide 17: Cortex-M0+ memory map
Figure 7: Cortex-M0+ memory map
Notes: Von Neumann model

## Slide 18: Assembly basics

## Slide 19: Assembly general considerations
Generally speaking, every assembly language code might be structured as follows
label
mnemonic operand1, operand2, …, ; comments
“label” is any word used as a reference for address location.
  Optional for some instructions.
  Used by branch instructions.
“mnemonic” is the name of the instruction.
“operands” for data processing instructions in ARMv6-M, first word after mnemonic is the destination of the operation. Following operands determine the source of the operation.
Comments are defined after “;” character.

## Slide 20: Assembly general considerations
Number of operands depend on the type of the instruction.
# symbol is used for specifying a constant (immediate) value.
  adds, r0, r1, #0xA ; r0 = r1 + 10 in hexadecimal
  adds, r0, r1, r2 ; r0 = r1 + r2
  ; Same mnemonic, different operands
  Types of operands for each instruction are defined by the ARMv6-M reference manual.
  Not all instructions accept different types of operands.
Why are constants called immediate?

## Slide 21: Assembly general considerations
Constants
  Declared in compiler directives
  MY_CONSTANT EQU 0x1234
  BIT_MASK EQU 0x000C0000
  These constants might be later used in the code
  adds, r0, r1, #MY_CONSTANT ; r0 = r1 + 0x1234

## Slide 22: C and its assembly equivalent
Revisit ADDS instruction
C Code
a = b + c
ARM Assembly Code
; R0 = a, R1 = b, R2 = c
ADDS R0, R1, R2
Instructions with Registers

## Slide 23: C and its assembly equivalent
Instructions with Registers
C Code
a = a + 4;
b = a – 12;
ARM Assembly Code
; R0 = a, R1 = b
ADDS R0, R0, #4
SUBS R1, R0, #12

## Slide 24: C and its assembly equivalent
Instructions with Registers
MOV instruction might be used for generating a small constant
C Code
//int: 32-bit signed word
int a = 23;
int b = 0x45;
ARM Assembly Code
; R0 = a, R1 = b
MOV R0, #23
MOV R1, #0x45

## Slide 25: C and its assembly equivalent
Instructions with Registers
What about immediate values larger than 8 bits?
We will solve that (later) with LDR pseudo-instruction
C Code
//int: 32-bit signed word
int a = 23;
int b = 0x45;
ARM Assembly Code
; R0 = a, R1 = b
MOV R0, #23
MOV R1, #0x45

## Slide 26: Cortex-M0+ memory access instructions
Cortex-M0+ allows access to byte, half-word and word data sizes.
Data must be aligned.
Unaligned access result in an exception.

## Slide 27: Cortex-M0+ addressable memory
Each data byte has a unique address.
Word address = 32 bits or 4 bytes.
Addresses increment by 4.

## Slide 28: Cortex-M0+ memory alignment
Notes: Only aligned transfers are allowed
Addresses must be a multiple of the transfer size
Word tranfers can access 0x0, 0x4, 0x8, 0xC, etc
Half-word transfers can access 0x0, 0x2, 0x4, etc
Byte transfers can access 0x0, 0x1, 0x2, 0x3, etc
Unaligned transfers generate an exception

## Slide 29: Memory access instructions

## Slide 30: Cortex-M0+ memory access instructions
Reading from memory

## Slide 31: Memory access instructions - example
Memory read called load
Mnemonic: load register (LDR)
Format:
LDR R0, [R1, #12]
  Address calculation:
    add base address (R1) to the offset (12)
    address = (R1 + 12)
  Result:
    R0 holds the data at memory address (R1 + 12)
    Cortex-M0+ might only use low registers

## Slide 32: Cortex-M0+ memory access
Example: Read a word of data at memory address 8 into R3
  LDR address is given by the addition of a register and an immediate
  We might use a dummy register for this purpose
  Address = (R2 + 8) = 8
  R3 = 0x01EE2842 after load
ARM Assembly Code
MOV R2, #0
LDR R3, [R2, #8]
Reading Memory

## Slide 33: Cortex-M0+ memory access
Memory write are called stores
Mnemonic: store register (STR)
Writing Memory

## Slide 34: Cortex-M0+ memory access
Example: Store the value held in R7 into memory word 21.
We want to access word 21, which address should access?
Memory address = 4 x 21 = 84 = 0x54
ARM assembly code
MOV R5, #0
STR R7, [R5, #0x54]
Writing Memory

## Slide 35: Cortex-M0+ memory access
Address of a memory word must be multiplied by 4
Examples:
  Address of memory word 2 = 2 × 4 = 8
  Address of memory word 10 = 10 × 4 = 40
Recap: Accessing Memory

## Slide 36: Data processing instructions

## Slide 37: Cortex-M0+ data processing instructions
Arithmetic operations
Logical operations
Shifts/rotate
Multiplication
Data-processing Instructions

## Slide 38: Cortex-M0+ examples of logical operations
AND
ORR
EOR (XOR)
BIC (Bit Clear)
MVN (MoVe and NOT)
Logical Instructions

## Slide 39: Cortex-M0+ examples of logical operations
Logical Instructions: Examples

## Slide 40: Cortex-M0+ examples of logical operations
AND or BIC: useful for masking bits
  Example: Masking all but the least significant byte of a value
  0xF234012F AND 0x000000FF = 0x0000002F
  0xF234012F BIC 0xFFFFFF00 = 0x0000002F
  Useful for clearing individual configuration bits
ORR: useful for combining bit fields
  Example: Combine 0xF2340000 with 0x000012BC:
  0xF2340000 ORR 0x000012BC = 0xF23412BC
  Useful for setting specific bits
Logical Instructions: Uses

## Slide 41: Cortex-M0+ examples of logical operations
LSL: logical shift left
  Example: LSL R0, R7, #5 ; R0 = R7 << 5
LSR: logical shift right
  Example: LSR R3, R2, #31 ; R3 = R2 >> 31
ASR: arithmetic shift right
  Example: ASR R9, R11, R4 ; R9 = R11 >>> R47:0
ROR: rotate right
  Example: ROR R8, R1, #3 ; R8 = R1 ROR 3
Shift Instructions

## Slide 42: Cortex-M0+ examples of logical operations
Arithmetic shifts
  Sign bit must be considered in arithmetic shifts
Rotate instructions

## Slide 43: Cortex-M0+ examples of logical operations
Shift Instructions: Example 1
Immediate shift amount (5-bit immediate)
Shift amount: 0-31

## Slide 44: Cortex-M0+ examples of logical operations
Shift Instructions: Example 2
Register shift amount (uses low 8 bits of register)
Shift amount: 0-255

## Slide 45: Cortex-M0+ example of multiplication
MUL: 32 × 32 multiplication, 32-bit result
  MUL R1, R2, R3
  Result: R1 = (R2 x R3)31:0
Multiplication

## Slide 46
Data-processing Instructions
Conditional Execution
Branches
High-level Constructs:
  if/else statements
  for loops
  while loops
  arrays
  function calls
Programming Building Blocks

## Slide 47
Don’t always want to execute code sequentially
For example:
  if/else statements, while loops, etc.: only want to execute code if a condition is true
  branching: jump to another portion of code if a condition is true
Conditional Execution

## Slide 48
Don’t always want to execute code sequentially
For example:
  if/else statements, while loops, etc.: only want to execute code if a condition is true
  branching: jump to another portion of code if a condition is true
ARM includes condition flags that can be:
  set by an instruction
  used to conditionally execute an instruction
Conditional Execution

## Slide 49
Flag | Name | Description
N | Negative | Instruction result is negative
Z | Zero | Instruction results in zero
C | Carry | Instruction causes an unsigned carry out
V | oVerflow | Instruction causes an overflow
ARM Condition Flags

## Slide 50
Set by ALU (recall from Chapter 5)
Held in Current Program Status Register (CPSR)
ARM Condition Flags
Flag | Name | Description
N | Negative | Instruction result is negative
Z | Zero | Instruction results in zero
C | Carry | Instruction causes an unsigned carry out
V | oVerflow | Instruction causes an overflow

## Slide 51
Review: ARM ALU

## Slide 52
Method 1: Compare instruction: CMP
  Example: CMP R5, R6
    Performs: R5-R6
    Does not save result
    Sets flags
Setting the Condition Flags: NZCV

## Slide 53
Method 1: Compare instruction: CMP
  Example: CMP R5, R6
    Performs: R5-R6
    Does not save result
    Sets flags. If result:
      Is 0, Z=1
      Is negative, N=1
      Causes a carry out, C=1
      Causes a signed overflow, V=1
Setting the Condition Flags: NZCV

## Slide 54
Method 1: Compare instruction: CMP
  Example: CMP R5, R6
    Performs: R5-R6
    Sets flags: If result is 0 (Z=1), negative (N=1), etc.
    Does not save result
Method 2: Append instruction mnemonic with S
Setting the Condition Flags: NZCV

## Slide 55
Method 1: Compare instruction: CMP
  Example: CMP R5, R6
    Performs: R5-R6
    Sets flags: If result is 0 (Z=1), negative (N=1), etc.
    Does not save result
Method 2: Append instruction mnemonic with S
  Example: ADDS R1, R2, R3
    Performs: R2 + R3
    Sets flags: If result is 0 (Z=1), negative (N=1), etc.
    Saves result in R1
Setting the Condition Flags: NZCV

## Slide 56
Instruction may be conditionally executed based on the condition flags
Condition of execution is encoded as a condition mnemonic appended to the instruction mnemonic
  Example: CMP R1, R2
  SUBNE R3, R5, R8
        NE: condition mnemonic
        SUB will only execute if R1 ≠ R2
        (i.e., Z = 0)
Condition Mnemonics

## Slide 57
cond | Mnemonic | Name | CondEx
0000 | EQ | Equal | 
0001 | NE | Not equal | 
0010 | CS / HS | Carry set / Unsigned higher or same | 
0011 | CC / LO | Carry clear / Unsigned lower | 
0100 | MI | Minus / Negative | 
0101 | PL | Plus / Positive of zero | 
0110 | VS | Overflow / Overflow set | 
0111 | VC | No overflow / Overflow clear | 
1000 | HI | Unsigned higher | 
1001 | LS | Unsigned lower or same | 
1010 | GE | Signed greater than or equal | 
1011 | LT | Signed less than | 
1100 | GT | Signed greater than | 
1101 | LE | Signed less than or equal | 
1110 | AL (or none) | Always / unconditional | ignored
cond | Mnemonic | Name | CondEx
0000 | EQ | Equal | 
0001 | NE | Not equal | 
0010 | CS / HS | Carry set / Unsigned higher or same | 
0011 | CC / LO | Carry clear / Unsigned lower | 
0100 | MI | Minus / Negative | 
0101 | PL | Plus / Positive of zero | 
0110 | VS | Overflow / Overflow set | 
0111 | VC | No overflow / Overflow clear | 
1000 | HI | Unsigned higher | 
1001 | LS | Unsigned lower or same | 
1010 | GE | Signed greater than or equal | 
1011 | LT | Signed less than | 
1100 | GT | Signed greater than | 
1101 | LE | Signed less than or equal | 
1110 | AL (or none) | Always / unconditional | ignored
Condition Mnemonics

## Slide 58
Example:
  CMP R5, R9 ; performs R5-R9
  ; sets condition flags
  SUBEQ R1, R2, R3 ; executes if R5==R9 (Z=1)
  ORRMI R4, R0, R9 ; executes if R5-R9 is
  ; negative (N=1)
Conditional Execution

## Slide 59
Example:
  CMP R5, R9 ; performs R5-R9
  ; sets condition flags
  SUBEQ R1, R2, R3 ; executes if R5==R9 (Z=1)
  ORRMI R4, R0, R9 ; executes if R5-R9 is
  ; negative (N=1)
  Suppose R5 = 17, R9 = 23:
    CMP performs: 17 – 23 = -6 (Sets flags: N=1, Z=0, C=0, V=0)
    SUBEQ doesn’t execute (they aren’t equal: Z=0)
    ORRMI executes because the result was negative (N=1)
Conditional Execution

## Slide 60
Data-processing Instructions
Conditional Execution
Branches
High-level Constructs:
  if/else statements
  for loops
  while loops
  arrays
  function calls
Programming Building Blocks

## Slide 61
Branches enable out of sequence instruction execution
Types of branches:
  Branch (B)
    branches to another instruction
  Branch and link (BL)
    discussed later
Both can be conditional or unconditional
Branching

## Slide 62
The Stored Program

## Slide 63
ARM assembly
MOV R2, #17 ; R2 = 17
B TARGET ; branch to target
ORR R1, R1, #0x4 ; not executed
TARGET
SUB R1, R1, #78 ; R1 = R1 + 78
Unconditional Branching (B)

## Slide 64
ARM assembly
MOV R2, #17 ; R2 = 17
B TARGET ; branch to target
ORR R1, R1, #0x4 ; not executed
TARGET
SUB R1, R1, #78 ; R1 = R1 + 78
Labels (like TARGET) indicate instruction location. Labels can’t be reserved words (like ADD, ORR, etc.)
Unconditional Branching (B)

## Slide 65
ARM Assembly
MOV R0, #4 ; R0 = 4
ADD R1, R0, R0 ; R1 = R0+R0 = 8
CMP R0, R1 ; sets flags with R0-R1
BEQ THERE ; branch not taken (Z=0)
ORR R1, R1, #1 ; R1 = R1 OR R1 = 9
THERE
ADD R1, R1, 78 ; R1 = R1 + 78 = 87
The Branch Not Taken

## Slide 66
Programming Building Blocks
Data-processing Instructions
Conditional Execution
Branches
High-level Constructs:
  if/else statements
  for loops
  while loops
  arrays
  function calls

## Slide 67
C Code
if (i == j)
f = g + h;
f = f – i;
if Statement

## Slide 68
C Code
if (i == j)
f = g + h;
f = f – i;
ARM Assembly Code
;R0=f, R1=g, R2=h, R3=i, R4=j
CMP R3, R4 ; set flags with R3-R4
BNE L1 ; if i!=j, skip if block
ADD R0, R1, R2 ; f = g + h
L1
SUB R0, R0, R2 ; f = f - i
if Statement

## Slide 69
C Code
if (i == j)
f = g + h;
f = f – i;
ARM Assembly Code
;R0=f, R1=g, R2=h, R3=i, R4=j
CMP R3, R4 ; set flags with R3-R4
BNE L1 ; if i!=j, skip if block
ADD R0, R1, R2 ; f = g + h
L1
SUB R0, R0, R2 ; f = f - i
if Statement
Assembly tests opposite case (i != j) of high-level code (i == j)

## Slide 70
C Code
if (i == j)
f = g + h;
f = f – i;
ARM Assembly Code
;R0=f, R1=g, R2=h, R3=i, R4=j
CMP R3, R4 ; set flags with R3-R4
ADDEQ R0, R1, R2 ; if (i==j) f = g + h
SUB R0, R0, R2 ; f = f - i
if Statement: Alternate Code

## Slide 71
Alternate Assembly Code
;R0=f, R1=g, R2=h, R3=i, R4=j
CMP R3, R4 ; set flags with R3-R4
ADDEQ R0, R1, R2 ; if (i==j) f = g + h
SUB R0, R0, R2 ; f = f - i
if Statement: Alternate Code
Original
CMP R3, R4
BNE L1
ADD R0, R1, R2
L1
SUB R0, R0, R2

## Slide 72
Alternate Assembly Code
;R0=f, R1=g, R2=h, R3=i, R4=j
CMP R3, R4 ; set flags with R3-R4
ADDEQ R0, R1, R2 ; if (i==j) f = g + h
SUB R0, R0, R2 ; f = f - i
if Statement: Alternate Code
Original
CMP R3, R4
BNE L1
ADD R0, R1, R2
L1
SUB R0, R0, R2
Useful for short conditional blocks of code

## Slide 73
C Code
if (i == j)
f = g + h;
else
f = f – i;
if/else Statement
ARM Assembly Code

## Slide 74
C Code
if (i == j)
f = g + h;
else
f = f – i;
ARM Assembly Code
;R0=f, R1=g, R2=h, R3=i, R4=j
CMP R3, R4 ; set flags with R3-R4
BNE L1 ; if i!=j, skip if block
ADD R0, R1, R2 ; f = g + h
B L2 ; branch past else block
L1
SUB R0, R0, R2 ; f = f – i
L2
if/else Statement

## Slide 75
C Code
if (i == j)
f = g + h;
else
f = f – i;
ARM Assembly Code
;R0=f, R1=g, R2=h, R3=i, R4=j
CMP R3, R4 ; set flags with R3-R4
ADDEQ R0, R1, R2 ; if (i==j) f = g + h
SUBNE R0, R0, R2 ; else f = f - i
if/else Statement: Alternate Code

## Slide 76
Alternate Assembly Code
;R0=f, R1=g, R2=h, R3=i, R4=j
CMP R3, R4 ; set flags with R3-R4
ADDEQ R0, R1, R2 ; if (i==j) f = g + h
SUBNE R0, R0, R2 ; else f = f - i
if/else Statement: Alternate Code
Original
CMP R3, R4
BNE L1
ADD R0, R1, R2
B L2
L1
SUB R0, R0, R2
L2

## Slide 77
C Code
// determines the power
// of x such that 2x = 128
int pow = 1;
int x = 0;
while (pow != 128) {
pow = pow * 2;
x = x + 1;
}
ARM Assembly Code
while Loops

## Slide 78
C Code
// determines the power
// of x such that 2x = 128
int pow = 1;
int x = 0;
while (pow != 128) {
pow = pow * 2;
x = x + 1;
}
ARM Assembly Code
; R0 = pow, R1 = x
MOV R0, #1 ; pow = 1
MOV R1, #0 ; x = 0
WHILE
CMP R0, #128 ; R0-128
BEQ DONE ; if (pow==128) ; exit loop
LSL R0, R0, #1 ; pow=pow*2
ADD R1, R1, #1 ; x=x+1
B WHILE ; repeat loop
DONE
while Loops

## Slide 79
C Code
// determines the power
// of x such that 2x = 128
int pow = 1;
int x = 0;
while (pow != 128) {
pow = pow * 2;
x = x + 1;
}
ARM Assembly Code
; R0 = pow, R1 = x
MOV R0, #1 ; pow = 1
MOV R1, #0 ; x = 0
WHILE
CMP R0, #128 ; R0-128
BEQ DONE ; if (pow==128) ; exit loop
LSL R0, R0, #1 ; pow=pow*2
ADD R1, R1, #1 ; x=x+1
B WHILE ; repeat loop
DONE
Assembly tests for the opposite case (pow == 128) of the C code (pow != 128).
while Loops

## Slide 80
for (initialization; condition; loop operation)
statement
initialization: executes before the loop begins
condition: is tested at the beginning of each iteration
loop operation: executes at the end of each iteration
statement: executes each time the condition is met
for Loops

## Slide 81
C Code
// adds numbers from 1-9
int sum = 0
for (i=1; i!=10; i=i+1)
sum = sum + i;
ARM Assembly Code
for Loops

## Slide 82
C Code
// adds numbers from 1-9
int sum = 0
for (i=1; i!=10; i=i+1)
sum = sum + i;
ARM Assembly Code
; R0 = i, R1 = sum
MOV R0, #1 ; i = 1
MOV R1, #0 ; sum = 0
FOR
CMP R0, #10 ; R0-10
BEQ DONE ; if (i==10) ; exit loop
ADD R1, R1, R0 ; sum=sum + i
ADD R0, R0, #1 ; i = i + 1
B FOR ; repeat loop
DONE
for Loops

## Slide 83
In ARM, decremented loop variables are more efficient
for Loops: Decremented Loops

## Slide 84
C Code
// adds numbers from 1-9
int sum = 0
for (i=9; i!=0; i=i-1)
sum = sum + i;
ARM Assembly Code
; R0 = i, R1 = sum
MOV R0, #9 ; i = 9
MOV R1, #0 ; sum = 0
FOR
ADD R1, R1, R0 ; sum=sum + i
SUBS R0, R0, #1 ; i = i – 1
; and set flags
BNE FOR ; if (i!=0) ; repeat loop
In ARM, decremented loop variables are more efficient
for Loops: Decremented Loops

## Slide 85
C Code
// adds numbers from 1-9
int sum = 0
for (i=9; i!=0; i=i-1)
sum = sum + i;
ARM Assembly Code
; R0 = i, R1 = sum
MOV R0, #9 ; i = 9
MOV R1, #0 ; sum = 0
FOR
ADD R1, R1, R0 ; sum=sum + i
SUBS R0, R0, #1 ; i = i – 1
; and set flags
BNE FOR ; if (i!=0) ; repeat loop
In ARM, decremented loop variables are more efficient
Saves 2 instructions per iteration:
Decrement loop variable & compare: SUBS R0, R0, #1
Only 1 branch – instead of 2
for Loops: Decremented Loops

## Slide 86
Programming Building Blocks
Data-processing Instructions
Conditional Execution
Branches
High-level Constructs:
  if/else statements
  for loops
  while loops
  arrays
  function calls

## Slide 87
Access large amounts of similar data
  Index: access to each element
  Size: number of elements
Arrays

## Slide 88
5-element array
  Base address = 0x14000000 (address of first element, scores[0])
  Array elements accessed relative to base address
Arrays

## Slide 89
C Code
int array[5];
array[0] = array[0] * 8;
array[1] = array[1] * 8;
ARM Assembly Code
; R0 = array base address
Accessing Arrays

## Slide 90
C Code
int array[5];
array[0] = array[0] * 8;
array[1] = array[1] * 8;
ARM Assembly Code
; R0 = array base address
MOV R0, #0x60000000 ; R0 = 0x60000000
LDR R1, [R0] ; R1 = array[0]
LSL R1, R1, 3 ; R1 = R1 << 3 = R1*8
STR R1, [R0] ; array[0] = R1
LDR R1, [R0, #4] ; R1 = array[1]
LSL R1, R1, 3 ; R1 = R1 << 3 = R1*8
STR R1, [R0, #4] ; array[1] = R1
Accessing Arrays

## Slide 91
C Code
int array[200];
int i;
for (i=199; i >= 0; i = i - 1)
array[i] = array[i] * 8;
ARM Assembly Code
; R0 = array base address, R1 = i
Arrays using for Loops

## Slide 92
C Code
int array[200];
int i;
for (i=199; i >= 0; i = i - 1)
array[i] = array[i] * 8;
ARM Assembly Code
; R0 = array base address, R1 = i
MOV R0, 0x60000000
MOV R1, #199
FOR
LDR R2, [R0, R1, LSL #2] ; R2 = array(i)
LSL R2, R2, #3 ; R2 = R2<<3 = R3*8
STR R2, [R0, R1, LSL #2] ; array(i) = R2
SUBS R0, R0, #1 ; i = i – 1
; and set flags
BPL FOR ; if (i>=0) repeat loop
Arrays using for Loops

## Slide 93
American Standard Code for Information Interchange
Each text character has unique byte value
  For example, S = 0x53, a = 0x61, A = 0x41
  Lower-case and upper-case differ by 0x20 (32)
ASCII Code

## Slide 94
Cast of Characters

## Slide 95
Programming Building Blocks
Data-processing Instructions
Conditional Execution
Branches
High-level Constructs:
  if/else statements
  for loops
  while loops
  arrays
  function calls

## Slide 96
Caller: calling function (in this case, main)
Callee: called function (in this case, sum)
C Code
void main()
{
int y;
y = sum(42, 7);
...
}
int sum(int a, int b)
{
return (a + b);
}
Function Calls

## Slide 97
Caller:
  passes arguments to callee
  jumps to callee
Function Conventions

## Slide 98
Caller:
  passes arguments to callee
  jumps to callee
Callee:
  performs the function
  returns result to caller
  returns to point of call
  must not overwrite registers or memory needed by caller
Function Conventions

## Slide 99
Call Function: branch and link
BL
Return from function: move the link register to PC: MOV PC, LR
Arguments: R0-R3
Return value: R0
ARM Function Conventions

## Slide 100
C Code
int main() {
simple();
a = b + c;
}
void simple() {
return;
}
ARM Assembly Code
0x00000200 MAIN BL SIMPLE
0x00000204 ADD R4, R5, R6
...
0x00401020 SIMPLE MOV PC, LR
Function Calls

## Slide 101
C Code
int main() {
simple();
a = b + c;
}
void simple() {
return;
}
ARM Assembly Code
0x00000200 MAIN BL SIMPLE
0x00000204 ADD R4, R5, R6
...
0x00401020 SIMPLE MOV PC, LR
Function Calls
void means that simple doesn’t return a value

## Slide 102
C Code
int main() {
simple();
a = b + c;
}
void simple() {
return;
}
BL branches to SIMPLE
LR = PC + 4 = 0x00000204
MOV PC, LR makes PC = LR
(the next instruction executed is at 0x00000200)
ARM Assembly Code
0x00000200 MAIN BL SIMPLE
0x00000204 ADD R4, R5, R6
...
0x00401020 SIMPLE MOV PC, LR
Function Calls

## Slide 103
ARM conventions:
Argument values: R0 - R3
Return value: R0
Input Arguments and Return Value

## Slide 104
C Code
int main()
{
int y;
...
y = diffofsums(2, 3, 4, 5); // 4 arguments
...
}
int diffofsums(int f, int g, int h, int i)
{
int result;
result = (f + g) - (h + i);
return result; // return value
}
Input Arguments and Return Value

## Slide 105
ARM Assembly Code
; R4 = y
MAIN
...
MOV R0, #2 ; argument 0 = 2
MOV R1, #3 ; argument 1 = 3
MOV R2, #4 ; argument 2 = 4
MOV R3, #5 ; argument 3 = 5
BL DIFFOFSUMS ; call function
MOV R4, R0 ; y = returned value
...
; R4 = result
DIFFOFSUMS
ADD R8, R0, R1 ; R8 = f + g
ADD R9, R2, R3 ; R9 = h + i
SUB R4, R8, R9 ; result = (f + g) - (h + i)
MOV R0, R4 ; put return value in R0
MOV PC, LR ; return to caller
Input Arguments and Return Value

## Slide 106
ARM Assembly Code
; R4 = result
DIFFOFSUMS
ADD R8, R0, R1 ; R8 = f + g
ADD R9, R2, R3 ; R9 = h + i
SUB R4, R8, R9 ; result = (f + g) - (h + i)
MOV R0, R4 ; put return value in R0
MOV PC, LR ; return to caller
diffofsums overwrote 3 registers: R4, R8, R9
diffofsums can use stack to temporarily store registers
Input Arguments and Return Value

## Slide 107
Memory used to temporarily save variables
Like stack of dishes, last-in-first-out (LIFO) queue
Expands: uses more memory when more space needed
Contracts: uses less memory when the space no longer needed
The Stack

## Slide 108
Grows down (from higher to lower memory addresses)
Stack pointer: SP points to top of the stack
The Stack
Stack expands by 2 words

## Slide 109
Called functions must have no unintended side effects
But diffofsums overwrites 3 registers: R4, R8, R9
ARM Assembly Code
; R4 = result
DIFFOFSUMS
ADD R8, R0, R1 ; R8 = f + g
ADD R9, R2, R3 ; R9 = h + i
SUB R4, R8, R9 ; result = (f + g) - (h + i)
MOV R0, R4 ; put return value in R0
MOV PC, LR ; return to caller
How Functions use the Stack

## Slide 110
ARM Assembly Code
; R2 = result
DIFFOFSUMS
SUB SP, SP, #12 ; make space on stack for 3 registers
STR R4, [SP, #-8] ; save R4 on stack
STR R8, [SP, #-4] ; save R8 on stack
STR R9, [SP] ; save R9 on stack
ADD R8, R0, R1 ; R8 = f + g
ADD R9, R2, R3 ; R9 = h + i
SUB R4, R8, R9 ; result = (f + g) - (h + i)
MOV R0, R4 ; put return value in R0
LDR R9, [SP] ; restore R9 from stack
LDR R8, [SP, #-4] ; restore R8 from stack
LDR R4, [SP, #-8] ; restore R4 from stack
ADD SP, SP, #12 ; deallocate stack space
MOV PC, LR ; return to caller
Storing Register Values on the Stack

## Slide 111
Before call
During call
After call
The Stack during diffofsums Call

## Slide 112
Preserved Callee-Saved | Nonpreserved Caller-Saved
R4-R11 | R12
R14 (LR) | R0-R3
R13 (SP) | CPSR
stack above SP | stack below SP
Registers

## Slide 113
ARM Assembly Code
; R2 = result
DIFFOFSUMS
STR R4, [SP, #-4]! ; save R4 on stack
ADD R8, R0, R1 ; R8 = f + g
ADD R9, R2, R3 ; R9 = h + i
SUB R4, R8, R9 ; result = (f + g) - (h + i)
MOV R0, R4 ; put return value in R0
LDR R4, [SP], #4 ; restore R4 from stack
MOV PC, LR ; return to caller
Storing Saved Registers only on Stack

## Slide 114
ARM Assembly Code
; R2 = result
DIFFOFSUMS
STR R4, [SP, #-4]! ; save R4 on stack
ADD R8, R0, R1 ; R8 = f + g
ADD R9, R2, R3 ; R9 = h + i
SUB R4, R8, R9 ; result = (f + g) - (h + i)
MOV R0, R4 ; put return value in R0
LDR R4, [SP], #4 ; restore R4 from stack
MOV PC, LR ; return to caller
Notice code optimization for expanding/contracting stack
Storing Saved Registers only on Stack

## Slide 115
ARM Assembly Code
STR LR, [SP, #-4]! ; store LR on stack
BL PROC2 ; call another function
...
LDR LR, [SP], #4 ; restore LR from stack
jr $ra ; return to caller
Nonleaf Function

## Slide 116
C Code
int f1(int a, int b) {
int i, x;
x = (a + b)*(a − b);
for (i=0; i<a; i++)
x = x + f2(b+i);
return x;
}
int f2(int p) {
int r;
r = p + 5;
return r + p;
}
Nonleaf Function Example

## Slide 117
C Code
int f1(int a, int b) {
int i, x;
x = (a + b)*(a − b);
for (i=0; i<a; i++)
x = x + f2(b+i);
return x;
}
int f2(int p) {
int r;
r = p + 5;
return r + p;
}
Nonleaf Function Example
ARM Assembly Code
; R0=a, R1=b, R4=i, R5=x
F1
PUSH {R4, R5, LR}
ADD R5, R0, R1
SUB R12, R0, R1
MUL R5, R5, R12
MOV R4, #0
FOR
CMP R4, R0
BGE RETURN
PUSH {R0, R1}
ADD R0, R1, R4
BL F2
ADD R5, R5, R0
POP {R0, R1}
ADD R4, R4, #1
B FOR
RETURN
MOV R0, R5
POP {R4, R5, LR}
MOV PC, LR
; R0=p, R4=r
F2
PUSH {R4}
ADD R4, R0, 5
ADD R0, R4, R0
POP {R4}
MOV PC, LR

## Slide 118
Nonleaf Function Example
ARM Assembly Code
; R0=a, R1=b, R4=i, R5=x
F1
PUSH {R4, R5, LR} ; save regs
ADD R5, R0, R1 ; x = (a+b)
SUB R12, R0, R1 ; temp = (a-b)
MUL R5, R5, R12 ; x = x*temp
MOV R4, #0 ; i = 0
FOR
CMP R4, R0 ; i < a?
BGE RETURN ; no: exit loop
PUSH {R0, R1} ; save regs
ADD R0, R1, R4 ; arg is b+i
BL F2 ; call f2(b+i)
ADD R5, R5, R0 ; x = x+f2(b+i)
POP {R0, R1} ; restore regs
ADD R4, R4, #1 ; i++
B FOR ; repeat loop
RETURN
MOV R0, R5 ; return x
POP {R4, R5, LR} ; restore regs
MOV PC, LR ; return
; R0=p, R4=r
F2
PUSH {R4} ; save regs
ADD R4, R0, 5 ; r = p+5
ADD R0, R4, R0 ; return r+p
POP {R4} ; restore regs
MOV PC, LR ; return

## Slide 119
Stack during Nonleaf Function
At beginning of f1
Just before calling f2
After calling f2

## Slide 120
C Code
int factorial(int n) {
if (n <= 1)
return 1;
else
return (n * factorial(n-1));
}
Recursive Function Call

## Slide 121
ARM Assembly Code
0x94 FACTORIAL STR R0, [SP, #-4]! ;store R0 on stack
0x98 STR LR, [SP, #-4]! ;store LR on stack
0x9C CMP R0, #2 ;set flags with R0-2
0xA0 BHS ELSE ;if (r0>=2) branch to else
0xA4 MOV R0, #1 ; otherwise return 1
0xA8 ADD SP, SP, #8 ; restore SP 1
0xAC MOV PC, LR ; return
0xB0 ELSE SUB R0, R0, #1 ; n = n - 1
0xB4 BL FACTORIAL ; recursive call
0xB8 LDR LR, [SP], #4 ; restore LR
0xBC LDR R1, [SP], #4 ; restore R0 (n) into R1
0xC0 MUL R0, R1, R0 ; R0 = n*factorial(n-1)
0xC4 MOV PC, LR ; return
Recursive Function Call

## Slide 122
ARM Assembly Code
0x94 FACTORIAL STR R0, [SP, #-4]!
0x98 STR LR, [SP, #-4]!
0x9C CMP R0, #2
0xA0 BHS ELSE
0xA4 MOV R0, #1
0xA8 ADD SP, SP, #8
0xAC MOV PC, LR
0xB0 ELSE SUB R0, R0, #1
0xB4 BL FACTORIAL
0xB8 LDR LR, [SP], #4
0xBC LDR R1, [SP], #4
0xC0 MUL R0, R1, R0
0xC4 MOV PC, LR
Recursive Function Call
C Code
int factorial(int n) {
if (n <= 1)
return 1;
else
return (n * factorial(n-1));
}

## Slide 123
Before call
During call
After call
Stack during Recursive Call

## Slide 124
Caller
  Puts arguments in R0-R3
  Saves any needed registers (LR, maybe R0-R3, R8-R12)
  Calls function: BL CALLEE
  Restores registers
  Looks for result in R0
Callee
  Saves registers that might be disturbed (R4-R7)
  Performs function
  Puts result in R0
  Restores registers
  Returns: MOV PC, LR
Function Call Summary