## Slide 1: Fixed-point and floating-point numbers

## Slide 2: References
The following material has been adopted and adapted from
Patterson, D. A., Hennessy, J. L., Computer Organization and design: The hardware/software interface – ARM edition, Morgan Kaufmann, 2017.
S. L. Harris and D. M. Harris, Digital design and computer architecture - ARM edition, Morgan Kaufmann, 2016.

## Slide 3: Numbers is digital systems
How is information represented in digital systems?
How do computers represent information?

## Slide 4: Numbers is computer systems
Fixed-point representation
  Integers – limited precision
  Non-integers – limited precision
Floating-point representation
  Real-world numbers
  Extremely large or extremely small numbers

## Slide 5: Fixed-point representation

## Slide 6: Fixed-point integer representation
Unsigned.
Sign & magnitude.
One’s complement.
Two’s complement.

## Slide 7: Signed integer representation

## Slide 8: Fixed-point integer representation
Unsigned.
Sign & magnitude.
One’s complement.
Two’s complement.
From all these binary integer representations, which one is most used in computer systems?

## Slide 9: Two’s complement integer range
Q: What’s the range (minimum and maximum values that can be represented) of an N-bit two’s complement number?
A:
For example, an 8-bit two’s complement number may represent values in the range
    =

## Slide 10: Two’s complement integer range
Q: What’s the minimum number of bits N required for representing decimal number D?
A:
Example: How many bits are required for representing the decimal number 12345?
A:

## Slide 11: Fixed-point numbers
What about real numbers?

## Slide 12: Fixed-point real numbers
Real numbers may not be represented with integer numbers.
    integer a,b;
    a = 1.5;
    b = a + a; // b = ?
Fixed-point representation allows real number representation with limited precision.
  Qm.n representation
    m  number of bits for representing integer part.
    n  number of bits for representing non-integer part.
    Range
    Resolution is

## Slide 13: Fixed-point real numbers
Qm.n example:
  What is the range of Q4.4 representation?
Qm.n example:
  What is the decimal value of the Q4.4 number 1000.0001?
    We first take the 2’s complement of the number
      0111.1111, which is 7.9375 in decimal
    Therefore, Q4.4 1000.0001 represents –7.9375 decimal

## Slide 14: Fixed-point in real-world applications
Fixed-point representation is suitable for embedded applications requiring limited degree of fractional precision.
  DOOM (1993 videogame) originally used a Q16.16 format for all non-integer operations https://doomwiki.org/wiki/Fixed_point
What about high-precision applications?

## Slide 15: Fixed-point limitations
Example:
  Consider Avogadro’s number:
    How many bits would you need to represent Avogadro’s number?
79
  What about a very small number such as Planck’s constant:
    How many bits (fractional fixed-point) would you need to represent Planck’s constant?
  We would need at least bits for representing both numbers.
    Not feasible, waste of resources.
    What if we need even smaller or larger numbers?

## Slide 16: Floating-point representation

## Slide 17: Floating-point
Scientific notation
    Sign
    Mantissa/significant
    Base with Exponent
Normalized scientific notation
  Absolute value of integer part is in the range
   1
Binary numbers may also be represented in scientific notation
normalized
not normalized
normalized
not normalized

## Slide 18: Floating-point
As the name suggest, binary point is not fixed.
Representation for non-integral numbers
  Including very small and very large numbers
  For simplicity, we’ll show the exponent in decimal.
Programming languages refer to this representation as float and double types.

## Slide 19: Floating-point standard
Defined by IEEE Std 754-1985
Developed in response to divergence of representations
  Portability issues for scientific code
Now almost universally adopted
Two representations
  Single precision (32-bit)
  Double precision (64-bit)
Simplifies exchange of data, arithmetic and increases accuracy.

## Slide 20: IEEE Floating-point format
sign: (0  non-negative, 1  negative)
Significand:
Normalized significand:
biased exponent = exponent + 127
  Ensures exponent is unsigned
  Single: bias = 127
  Double: bias = 1023
sign
mantissa
single: 8 bits double: 11 bits
single: 23 bits double: 52 bits
1 bit
Implicit 1
biased exponent

## Slide 21: IEEE Floating-point format
First example: 0.5 to single-precision floating-point
  =
  For simplification, we are using decimal notation for the exponent
  From this, we can gather the following information:
    sign: 0
    mantissa: 0 (normalized)
    exponent: -1
  Everything together:
    biased exponent= or
    Normalized floating-point:
sign
mantissa
single: 8 bits double: 11 bits
single: 23 bits double: 52 bits
1 bit
biased exponent

## Slide 22: IEEE Floating-point format
First example: 0.5 to single-precision floating-point
What about 0.5 in double-precision?
  0000000000000000000000000000000000000000000000000000
This 1 is not actually required here
sign
mantissa
single: 8 bits double: 11 bits
single: 23 bits double: 52 bits
1 bit
biased exponent

## Slide 23: Floating-point example
Represent –0.75
  –0.75 = (–1)1 × 1.12 × 2–1
  sign = 1
  mantissa = 1000…002
  biased exponent = –1 + bias
    Single: –1 + 127 = 126 = 011111102
    Double: –1 + 1023 = 1022 = 011111111102
Single: 1011111101000…00
Double: 1011111111101000…00

## Slide 24: Floating-point example
Represent 5.625
  5.625 = (–1)0 × 1.011012 × 22
  sign = 0
  mantissa = 011010000000000000000002
  biased exponent = 2 + bias
    Single: 2 + 127 = 129 = 100000012
    Double: 2 + 1023 = 1024 = 100000000012
Single: 01000000101101000000000000000000
Double: 0100000000010110100…00

## Slide 25: Floating-point example
What number is represented by the single-precision float
11000000101000000000000000000000
  sign = 1
  biased exponent = 100000012 = 129
  mantissa = 01000…002
1 (1.012) 2(129 – 127)
  22
sign
exponent
mantissa
single: 8 bits double: 11 bits
single: 23 bits double: 52 bits
1 bit
Remember that this 1 is always implied!

## Slide 26: Single precision range
Exponents 00000000 and 11111111 reserved
Smallest value
exponent: 00000001  actual exponent = 1 – 127 = –126
Fraction: 000…00  significand = 1.0
±1.0 × 2–126 ≈ ±1.2 × 10–38
Largest value
exponent: 11111110  actual exponent = 254 – 127 = +127
Fraction: 111…11  significand ≈ 2.0
±2.0 × 2+127 ≈ ±3.4 × 10+38

## Slide 27: Double precision range
Exponents 00000000000 and 11111111111 reserved
Smallest value
Exponent: 00000000001  actual exponent = 1 – 1023 = –1022
Fraction: 000…00  significand = 1.0
±1.0 × 2–1022 ≈ ±2.2 × 10–308
Largest value
exponent: 11111111110  actual exponent = 2046 – 1023 = +1023
Fraction: 111…11  significand ≈ 2.0
±2.0 × 2+1023 ≈ ±1.8 × 10+308

## Slide 28: Floating-point precision
Relative precision
  Single: approx. decimal digits
  Double: approx. decimal digits

## Slide 29: Floating-point special representation
Denormal numbers
  In normalised numbers, significand have an implicit leading 1
  Denormal numbers have a leading 0 in the significand.
  Biased exponent is 0.
  These numbers allow to represent numbers smaller than the smaller normalised number, as well as special representation such as and NaN ).

## Slide 30: Denormal numbers
Smaller than normal numbers.
Zero
  sign = 0,1
  biased exponent = 0
  mantissa = 0
Two representations of 0.0!

## Slide 31: Denormalized numbers
Smallest denormalized value
Single precision:
Single precision: 〖±2^(−23)×2^(−126)≈1.4×10〗^(−45)
Largest denormalized value
Single precision:
Single precision: 〖±(1−2^(−23) )×2^(−126)≈±1.17×10〗^(−38)
Double precision:
Double precision: 〖±2^(−52)×2^(−1022)≈4.9×10〗^(−324)
Double precision:
Double precision: 〖±(1−2^(−52) )×2^(−1022)≈±2.22×10〗^(−308)
Smallest denormalized value
Largest denormalized value

## Slide 32: Infinities and NaNs
Exponent = 111...1, mantissa = 000...0
  Can be used in subsequent calculations, avoiding need for overflow check
Exponent = 111...1, mantissa ≠ 000...0
  Not-a-Number (NaN)
  Indicates illegal or undefined result
    e.g., 0.0 / 0.0
  Can be used in subsequent calculations

## Slide 33: Floating-point special formats summary

## Slide 34: Floating-point addition

## Slide 35: Floating-point addition
1. Align decimal points
Shift number with smaller exponent
9.999 × 101 + 0.016 × 101
9.999 × 101 + 0.016 × 101 = 10.015 × 101
3. Normalize result & check for over/underflow
1.0015 × 102
4. Round and renormalize if necessary
1.002 × 102
2. Add significands
Consider a decimal example
Rounding up to 3 decimal places

## Slide 36: Floating-point addition
Consider a floating-point example
  or (0.5+-0.4375)
1. Align decimal points
Shift number with smaller exponent
〖1.000〗_2×2^(−1)+ −〖0.1110〗_2×2^(−1)
1.0002 × 2^(−1) + –0.1112 × 2^(−1) = 0.0012 × 2^(−1)
3. Normalize result & check for over/underflow
〖1.0〗_2×2^(−4)
4. Round and renormalize if necessary
〖1.0〗_2×2^(−4)=0.0625
2. Add significands
1. Align decimal points
3. Normalize result & check for over/underflow
4. Round and renormalize if necessary
2. Add significands

## Slide 37: Floating-point adder hardware
Much more complex than integer adder.
Doing it in one clock cycle would take too long.
  Much longer than integer operations.
  Slower clock would penalize all instructions.
Floating-point adder usually takes several cycles
  Can be pipelined

## Slide 38: Floating-point adder hardware
Step 1
Step 2
Step 3
Step 4

## Slide 39: Floating-point adder hardware
Step 1
Step 2
Step 3
Step 4

## Slide 40: Floating-point adder hardware
Step 1
Step 2
Step 3
Step 4

## Slide 41: Floating-point adder hardware
Step 1
Step 2
Step 3
Step 4

## Slide 42: Floating-point adder hardware
Step 1
Step 2
Step 3
Step 4

## Slide 43: Floating-point adder hardware
Step 1
Step 2
Step 3
Step 4

## Slide 44: Floating-point adder hardware
Step 1
Step 2
Step 3
Step 4

## Slide 45: Floating-point multiplication

## Slide 46: Floating-point multiplication
Consider a decimal example
1.110 × 1010 × 9.200 × 10^(−5)
1. Add exponents
For biased exponents, subtract bias from sum
New exponent = 10 + –5 = 5
2. Multiply significands
1.110 × 9.200 = 10.212  10.212 × 105
3. Normalize result & check for over/underflow
1.0212 × 106
4. Round and renormalize if necessary
1.021 × 106
5. Determine sign of result from signs of operands
+1.021 × 106
Consider a decimal example
1. Add exponents
For biased exponents, subtract bias from sum
New exponent = 10 + –5 = 5
2. Multiply significands
3. Normalize result & check for over/underflow
4. Round and renormalize if necessary
5. Determine sign of result from signs of operands

## Slide 47: Floating-point multiplication
Consider a floating-point example
in decimal, or
−14.25 ×3.125 in decimal, or
1. Add exponents
Unbiased: 3 + 1 = 4
Biased: (3 + 127) + (1 + 127)
Biased: (3 + 127) + (1 + 127)−127
2. Multiply significands
−1.110012×1.10012
3. Normalize result & check for over/underflow
with no over/underflow
1.01100100012×2^5 with no over/underflow
4. Round and renormalize if necessary
(no change)
1.01100100012×2^5(no change)
5. Determine sign of result from signs of operands
–1.01100100012×2^5= –44.53125
= 〖10.110010001〗_2
−1.110012×2^3×1.10012×2^1
= 4 + 254 – 127 = 4 + 127
 10.1100100012×2^4
Consider a floating-point example
1. Add exponents
2. Multiply significands
3. Normalize result & check for over/underflow
4. Round and renormalize if necessary
5. Determine sign of result from signs of operands

## Slide 48: Floating-point multiplication
What’s the floating-point of the previous result?
  sign = 1
  biased exponent
    Single precision:
    Double precision:
  mantissa =
  Floating point representation:
Single precision:
  Double precision:

## Slide 49: Floating-point arithmetic hardware
Floating-point multiplier is of similar complexity to floating-point adder.
  But uses a multiplier for significands instead of an adder.
Floating-point arithmetic hardware usually does
  Addition, subtraction, multiplication, division, reciprocal, square-root.
  Floating-point  integer conversion
Operations usually takes several cycles
  Can be pipelined

## Slide 50: Floating-point rounding

## Slide 51: Floating-point rounding
Let’s try to represent in floating-point.
  Represent in binary
    Integer part is 0
    Fractional part is:
    This sequences repeats infinite times!
    0.1 is not a machine number, which means, it may not be exactly represented in a computing system.

## Slide 52: Floating-point rounding
Our floating-point representation will have to be as close as possible to
Remember that mantissa is 23 and 52 bits for single- and double-precision, respectively.
IEEE employs rounding.
  If first extra bit is 1, we add 1 to the rest of the mantissa bits – This is rounding up
  If first extra bit is 0, we drop all extra bits – This is rounding down.
  Special case if extra bits are 1000….000
    Round up if last mantissa bit is 1
    Round down if last mantissa bit is 0

## Slide 53: Floating-point rounding
Rounded normalized value:
  We rounded up for this example
(single)
Floating-point representation:
Single:
Which represents the value of
0.100000001490116119384765625
Similarly, double precision represents 0.1 as
0.1000000000000000055511151231257827021181583404541015625

## Slide 54: Floating-point rounding
In your favourite programming language try the following code using float or double data types.
Is the result TRUE or FALSE?
Problems with accuracy
  Several failures (in some cases with fatal consequences) have been reported due to numerical errors.
  http://ta.twi.tudelft.nl/users/vuik/wi211/disasters.html

## Slide 55: Concluding remarks
Bits have no inherent meaning
  Interpretation depends on the application.
Computer representations of numbers
  Finite range and precision, even in double-precision floating-point representation.
  Need to account for this in programs.

## Slide 56: Concluding remarks
  ????