## Slide 1: TC2009B: Digital design Addition & Subtraction

## Slide 2: References
The following material has been adopted and adapted from
Patterson, D. A., Hennessy, J. L., Computer Organization and design: The hardware/software interface – ARM edition, Morgan Kaufmann, 2017.
S. L. Harris and D. M. Harris, Digital design and computer architecture - ARM edition, Morgan Kaufmann, 2016.

## Slide 3: Adder

## Slide 4: 1-bit adders

## Slide 5: 1-bit adders

## Slide 6: 1-bit adders

## Slide 7: Multibit adders
Types of carry propagate adders (CPAs):
  Ripple-carry (slow)
  Carry-lookahead (fast)
  Prefix (faster)
Carry-lookahead and prefix adders faster for large adders but require more hardware

## Slide 8: Ripple-Carry adder
Chain 1-bit adders together
Carry ripples through entire chain
Disadvantage: slow
  is the delay of a 1-bit full adder

## Slide 9: Carry-lookahead adder
Compute Cout for k-bit blocks using generate and propagate signals
Some definitions:
  Column i produces a carry out by either generating a carry out or propagating a carry in to the carry out
  Generate (Gi) and propagate (Pi) signals for each column:
    Generate: Column i will generate a carry out if Ai and Bi are both 1.
    Gi = Ai Bi
    Propagate: Column i will propagate a carry in to the carry out if Ai or Bi is 1.
    Pi = Ai + Bi
    Carry out: The carry out of column i (Ci) is:
    Ci = Ai Bi + (Ai + Bi )Ci-1 = Gi + Pi Ci-1

## Slide 10: Carry-lookahead adder
Now use column propagate and generate signals to compute block propagate and block generate signals for k-bit blocks, i.e.:
  Compute if a k-bit group will propagate a carry in (to the block) to the carry out (of the block)
  Compute if a k-bit group will generate a carry out (of the block)

## Slide 11: Carry-lookahead adder
Example: Block propagate and generate signals for 4-bit blocks (P3:0 and G3:0):
P3:0 = P3P2 P1P0
G3:0 = G3 + P3 (G2 + P2 (G1 + P1G0 ))
Generally,
Pi:j = PiPi-1 Pi-2…Pj
Gi:j = Gi + Pi (Gi-1 + Pi-1 (Gi-2 + Pi-2(Gi-3 +Pi-3(… Gj+1 + Pj+1Gj))
Ci = Gi:j + Pi:j Ci-1

## Slide 12: 32-bit Carry-lookahead with 4 blocks

## Slide 13: Carry-lookahead addition
Step 1: Compute Gi and Pi for all columns
Step 2: Compute G and P for k-bit blocks
Step 3: Cin propagates through each k-bit propagate/generate logic (meanwhile computing sums)
Step 4: Compute sum for most significant k-bit block

## Slide 14: Carry-lookahead adder delay
For N-bit CLA with k-bit blocks:
tCLA = tpg + tpg_block + (N/k – 1)tAND_OR + ktFA
where:
  tpg: delay to generate all Pi and Gi
  tpg_block : delay to generate all Pi:j and Gi:j
  tAND_OR : delay from Cin to Cout of final AND/OR gate in k-bit CLA block
An N-bit carry-lookahead adder is generally much faster than a ripple-carry adder for N > 16

## Slide 15: Prefix adder
Computes carry in (Ci-1) for each column, then computes sum:
Si = (Ai Å Bi) Å Ci
Computes G and P for 1-, 2-, 4-, 8-bit blocks, etc. until all Gi (carry in) known
stages

## Slide 16: Prefix adder
Carry is either generated in a column or propagated from a previous column.
Column -1 holds Cin, so
  G-1 = Cin, P-1 = 0
Carry in to column i = carry out of column i-1:
  Ci-1 = Gi-1:-1
Gi-1:-1: generate signal spanning columns i-1 to -1
Sum equation:
  Si = (Ai Å Bi) Å Gi-1:-1
Goal: Quickly compute G0:-1, G1:-1, G2:-1, G3:-1, G4:-1, G5:-1, … (called prefixes)

## Slide 17: Prefix adder
Generate and propagate signals for a block spanning bits i:j
  Gi:j = Gi:k + Pi:k Gk-1:j
  Pi:j = Pi:kPk-1:j
In words:
  Generate: block i:j will generate a carry if:
    upper part (i:k) generates a carry or
    upper part (i:k) propagates a carry generated in lower part (k-1:j)
  Propagate: block i:j will propagate a carry if both the upper and lower parts propagate the carry

## Slide 18: 16-bit prefix adder

## Slide 19: Prefix adder delay
tPA = tpg + log2N(tpg_prefix ) + tXOR
  tpg: delay to produce Pi, Gi (AND or OR gate)
  tpg_prefix: delay of black prefix cell (AND-OR gate)

## Slide 20: Adder delay comparison
Compare delay of 32-bit adder structures: ripple-carry, carry-lookahead, and prefix adders
Carry-lookahead has 4-bit blocks
2-input gate delay = 100 ps;
full adder delay = 300 ps
tripple = NtFA = 32(300 ps)
= 9.6 ns
tCLA = tpg + tpg_block + (N/k – 1)tAND_OR + ktFA
= [100 + 600 + (7)200 + 4(300)] ps
= 3.3 ns
tPA = tpg + log2N(tpg_prefix ) + tXOR
= [100 + log232(200) + 100] ps
= 1.2 ns

## Slide 21: Misc arithmetic circuits

## Slide 22: Subtractor

## Slide 23: Comparator

## Slide 25: Adder/subtractor circuit
How can we implement an adder/subtractor circuit reutilizing adder’s HW?